| Plenary | Doc. ECC(14)006 |
| --- | --- |
| 36th Meeting |  |
| Cluj-Napoca, 11th – 14th March 2014 |  |
| Date issued: | 18th February 2014 |
| Source: | ECC PT1 Chairman |
| Subject: | ECC PT1 Progress report |
| Group membership required to read? (Y/N) Summary The last ECC PT1 plenary was held in Roma (Italy) from 13 to 17 January 2014 at the invitation of the Italian Administration. This progress report highlights the issues where a decision from ECC is required (section 1). Additionally, this report provides some useful background information on issues which might be of interest for the 36th meeting of ECC (section 2). Proposal: ECC is invited: to consider the results of public consultation and to approve for publication the amended ECC DEC(11)06 (see section 1.1), to consider the organization of the work, the description of tasks to respond to the EC 700 MHz mandate and to give guidance where appropriate (see section 1.2), to approve for publication the amended ECC DEC(06)07 (see section 1.3), to consider the result of questionnaire on coverage obligation (see section 1.4) to consider and confirm the extension of the activity on Mobile Communications on Board Vessels (see section 1.5) to endorse the ECC PT1 work program (see section 1.6), to consider the deliverables (ECC Decisions and recommendations) for review by ECC PT1 (see section 1.7) and to provide guidance as appropriate, to note other issues for information in section 2 of this progress report. Background The last ECC PT1 plenary was held in Roma (Italy) from 13 to 17 January 2014 at the invitation of the Italian Administration. The meeting was attended by 114 delegates representing 25 CEPT Administrations, the ECO, other organisations and a number of operators and manufacturers. ECC PT1 #45 meeting has been co-located and scheduled in conjunction with the CPG PTD#5 meeting. This approach will be maintained due to the fact that most of participants of ECC PT1 are also CPG PTD participants. Items, where an action from ECC is required Final Approval of revised ECC DEC(11)06 “Harmonised frequency arrangements for mobile/fixed communications networks (MFCN) operating in the bands 3400-3600 MHz and 3600-3800 MHz” Taking into account the results from the last ECC (see ECC minutes), ECC PT1 resolved all the comments received during the public consultation (except those related to the channelling arrangements in the 3400-3600 MHz) and agreed on the updated ECC Decision (11)06 to be submitted to ECC for final approval (see Annex 1). Further to the public consultation, the revised deliverable has been largely improved. In particular, a correction in addition to the PC comments has been introduced: see Annex 4, Table 5, frequency range 3490 – 3500 MHz. This BEM element was previously stated as an e.i.r.p. level, which is incorrect, and has been modified to say “at the antenna port”. ECC PT1 assumed the same correction should be introduced into ECC Report 203 (corrigendum), CEPT Report 49 (corrigendum) and the corresponding EC Decision under revision process based on CEPT report 49. ECC SG provided advice on the update of those 2 reports. ECC is invited to consider the update of ECC report 203 and CEPT report 49 (see Annex 3) according to RoP 12.5.3 as proposed by ECC SG. Moreover, based on the decision at the last ECC meeting, ECC PT1 did not consider the comments related to the channelling arrangements in the 3400-3600 MHz band and has highlighted these comments in the resolution table for the ECC to address the issue as appropriate. ECC is invited to address those comments before the final approval of the revised ECC DEC(11)06 (see annex 2). ECC is invited to consider the result of public consultation and to approve for publication the revised ECC DEC(11) 06 EC 700 MHz mandate At the ECC#33 meeting, ECC confirmed ECC PT1 as the leading group to manage the development of the response to EC mandate on 700 MHz. This activity is conducted in conjunction with CPG PTD. In particular, common sessions ECC PT1/CPG PTD took place at the last ECC PT1 and CPG PTD meetings. Moreover a cooperation process is in place with WG FM/PT FM 49, WG FM/PT 51 and WG SE/ SE 7. ECC PT1 received feedback from PT FM 49 on PPDR parameters which are taken in due consideration in the on-going studies (in particular, studies on compatibility between the broadcasting service below 694 MHz and the mobile service in the band 694-790 MHz which are on-going in CPG PTD –see LS to this meeting). PT FM 49 mentioned that all the proposed options in ECC PT1 band plans would enable the implementation of all three different solutions for BB PPDR (dedicated, commercial and hybrid networks) which are under consideration. ECC PT1 intends to make further progress on the preferred 700 MHz band plan at its next meeting. ECC PT1 is also studying “BEM at 700 MHz” based on the block edge mask (BEM) concept. Activity will continue by correspondence. The current PPDR parameters provided by WG FM 49 have been taken in due consideration in this activity. This CG activity will also include the following issues: the machine-to-machine communication (provided that material on this topic is submitted) the PPDR DMO (provided that material on this topic is submitted) Concerning PMSE, ECC PT1 provided detailed WBB parameters including those on PPDR from FM 49 to WG SE/SE7 which will develop BEM for PMSE usage (wireless audio applications) in the duplex gap of the 700 MHz band plans under consideration. A feedback is expected at the next meeting. The analysis of possible impact on PMSE below 694 MHz in order to identify the relevant coexistence criteria will be done by ECC PT1 (CG activity on BEM 700 MHz). WG SE has been kept inform of that initiative. At the last meeting, ECC PT1 in a common session with CPG PTD, considered proposals on 700 MHz band plan in particular additional sub options of the option 1 (2x30 MHz Lower Duplexer APT band plan). No decision has been taken yet. Nevertheless, administrations shall be ready to contribute at the next meeting to the decision on a preferred 700 MHz band plan. ECC PT1 benefits also from the support of CPG PTD on the definition of the IMT user equipment Out of Band Emission limit required to protect the DTT reception. At the last meeting, CEPT administrations decided to limit the preliminary range of values for OOB emission limit to be considered in the studies to [-40...-46] dBm/(8 MHz) (for 10 MHz IMT channel). This is for a mobile UE uplink using the band plan options mentioned in the interim CEPT Report (see ECC(13)090 Annex 17 section “Preferred technical channelling arrangement in 694 -790 MHz”) with the Out of Band Emission (OOBE) limit to be met in an 8 MHz channel centred on 690 MHz and below. Further information will be collected from the industry. In particular, in order to define the IMT user equipment OOBE limit required to protect the DTT reception and to assess its impact on the broadcasting and mobile sectors, having in mind the aim to achieve economies of scale, substantial information on the following key elements from the industry is required: 1) Expected TV receiver ACS characteristics taking into account the evolution either ongoing or foreseen during the next 5 years. 2) Achievable ACLR characteristics of the IMT UE (in particular, using LTE), impact on mobile terminal cost and performance for the range of OOB emission limits taking into account on-going activities in R&D, the relationship with channel bandwidth (BW 10 MHz is assumed for Europe), battery life, complexity of design, other relevant aspects, and the evolution foreseen for the next 5 years. Other information that the broadcasting and mobile sectors consider as relevant for the subject is welcome. This information to be provided by 11 April 2014 will be also helpful in order to make a decision on the preferred 700 MHz band plan. ECC PT1 intends to finalize the draft CEPT report for approval for public consultation at its next plenary meeting. A skeleton of the draft CEPT has been developed at the last meeting with the support of ECO. ECC is invited to consider the organization of the work, the description of tasks to respond to the EC 700 MHz mandate and to give guidance where appropriate (see ANNEX 4). At the last meeting, ECC PT1 noted the letter from Cable Europe on EC mandate 700 MHz. In particular, ECC PT1 conducted studies on radio issues with support of various entities (CPG PTD and WG SE). Nevertheless, ECC keeps, where appropriate, ETSI (and or other relevant SDOs like e.g. CENELEC) aware of the regulatory changes on the "radio side" so that they can see if they need to change anything on their standardization side. This letter from Cable Europe has been transferred to ECC for further consideration. ECC is invited to consider the letter from Cable Europe and to develop a response where appropriate. Final approval of ECC DEC(06)07 on the “harmonised use of airborne GSM and LTE systems in the frequency bands “1710-1785 and 1805-1880 MHz” and airborne UMTS systems in the frequency bands 1920-1980 MHz and 2110-2170 MHz” ECC PT1 resolved the comment received and agreed to submit the decision to ECC(06)07 for final approval. Only one editorial comment has been introduced. ECC is invited to consider and to approve for publication the revised ECC/DEC/(06)07 (see ANNEX 5) Coverage Obligations The last ECC meeting noted the need to assess the various coverage obligations in force in CEPT countries and how they are measured and enforced. ECC invited ECC/PT1 to develop a questionnaire on coverage obligations and how they are controlled and to report at this ECC meeting. Based on a proposal resulting from correspondence group activity, ECC PT1 agreed on a questionnaire which has been circulated to CEPT administrations for responses before 17 February. Summary and results of responses are currently under analysis by an ECC PT1 Correspondence Group at the time of publication of this progress report. An ad hoc input document will be delivered by ECC PT1 before this ECC meeting. ECC is invited to consider the results of questionnaire on coverage obligations and to decide on the way forward. Mobile Communications on Board Vessels ECC PT1 is currently developing by correspondence a draft ECC report covering coexistence of MCV system (UMTS (2 GHz), LTE (1800 MHz) and LTE (2.6 GHz) with land-based systems and additional information about unintended roaming. This draft report, entitled “Compatibility between Mobile Communication services on board Vessels (MCV) and land-based networks”, aims at (1) studying the possible use of UMTS in the 2GHz band and LTE in 2.6GHz band by MCV; (2) studying the possible use of LTE in the 1800 MHz band by MCV; (3) taking into account the deployment of LTE for land-based networks in existing MCV bands (i.e. 900MHz and 1800MHz bands); (4) proposing solutions to avoid unintended roaming for the cases (1) and (2). ECC#32 noted the need to revise ECC/DEC/(08)08 to include other technologies and other frequency bands in addition to the 900 MHz and 1800 MHz : usage UMTS in the 2GHz band and LTE in 2.6GHz band by MCV. Compared to these above initial assumptions for future MCV systems, ECC PT1 informs ECC on an additional study on the possible use of LTE in the 1800 MHz band by MCV. The revision of ECC/DEC/(08)08 will be done based on the results of those studies. ECC is invited to endorse the extension of scope of activity on MCV to include also a study on possible use of LTE in the 1800 MHz band by MCV. Updated ECC PT1 work program The ECC PT1 Work Programme was reviewed and agreed at the last meeting In particular, a preliminary work item proposed for the WRC-15 Agenda Item 10 work in support of CPG-PTA has been added. “To support CPG-PTA in the development of a proposal for a WRC-18 Agenda Item on “Future IMT systems above 6 GHz”” The Work Programme was also updated regarding L-band, 2300-2400 MHz, TDD Synchronization, cross-border coordination and MCV co-existence. ECC is invited to endorse the ECC PT1 work program (see ANNEX 6) ECC Decisions and recommendations for review by ECC PT1 ECC PT1 decided to formally initiate the regular review (5 years period) of the ECC Decisions hereafter and is seeking inputs so that the review process can progress at the next meeting (see annex 7). This concerns the following ECC Decisions: • ERC/DEC/(94)03 on the frequency band to be designated for the coordinated introduction of the Digital European Cordless Telecommunications system • ECC/DEC/(02)06 on the designation of frequency band 2500-2690 MHz for UMTS/IMT-2000 • ECC/DEC/(05)05 on harmonised utilisation of spectrum for IMT-200/UMTS systems operating within the band 2500-2690 MHz • ECC/DEC/(09)03 on harmonised conditions for Mobile/Fixed Communications Networks (MFCN) operating in the band 790-862 MHz ECC is invited, if needed, to give further guidance on that issue. Others issues for information Cross border coordination ECC PT1 received a proposal at its last meeting to consider 3 frequency ranges (below 1 GHz, between 1 and 3 GHz, and above 3 GHz) in order to develop a generic recommendation on cross border coordination. ECC PT1 agreed to continue the work in the correspondence group in order to progress on the issue taken into account also previous inputs. Interested parties are invited to join the CG activity: To study the possibility to develop a new generic recommendation for new frequency bands To consider evolution of current ECC framework in the light of the previous results while minimizing the impact on the existing agreements based on the actual ECC recommendations. 3,4-3,8 GHz TDD networks synchronisation ECC PT1 is developing an ECC Report on TDD network synchronisation. This report is focusing on practical technical solutions of TDD networks synchronisation to be implemented by adjacent TDD network operators. Further to approval by ECC PT1, ECC SG agreed that due to the nature of the draft ECC report the public consultation could be launched by ECC PT1 itself, if no objections to proceed to public Consultation are received by the Office from any CEPT Member. ECO Report 03 “mobile licensing in CEPT countries” ECC PT1 decided that it was too early to move to the new procedure of generating the content of ECO Report 03 from EFIS data base at this point in time. This would mean loosing a significant amount of information as currently contained in ECO Report 03. In consequence, ECC PT1 agreed to maintain the current practices. The regular annual update through the ECO as it has been done in past years has been launched. Administrations are invited to respond to ECO before the 13rd of March in order to update the ECO report 03. Moreover, ECC PT1 developed a guidance document in order to increase the consistency of national entries for the “mobile bands” in the EFIS database for the purpose of generation of ECO Report 03 on the licensing of “mobile bands” in CEPT from the “Right of use” module of EFIS. More consistency of national entries for the “mobile bands” is a prerequisite to generate the content of ECO Report 03 from EFIS. Administrations are invited to respond to take into account this guidance document when updating EFIS. The above information has been shared with WG FM. Others issues ECC PT1 agreed RIS implementations for ERC Decision (98)22 and ECC Decision (06)13 which had recently been revised and finally approved by the ECC. ECC PT1 agreed to transfer the information to EFIS/MG for uploading into the ECO Documentation Database. Details on CG activities between ECC PT1 plenary meetings are available on the ECC PT1 web site. Meeting dates 2014 • 28 April -2 May Luxembourg • 1-5 September Croatia (Location TBD) 2015 • 19-23 January Edinburgh - UK • 20-24 April (TBD) Lithuania • 22 - 26 June (TBD) Switzerland 2016 • xx January (TBD) Finland • May (TBD) • September (TBD) CPG PTD will be co-located and will be held the same week in conjunction with ECC PT1 in 2014/15. *Meeting dates subject to modification. ECC PT1 : 3 days meetings in 2016 ECC PT1 is seeking for possible hosts in 2016. |

Annexes

- Revised ECC DEC(11)06

- Resolution of comments from PC on draft revised ECC DEC(11)06

- Possible corrigendum ECC report 203 – CEPT report 49

- EC 700 MHz mandate – descriptions of tasks, organisation of work

- Revised ECC DEC (06) 07 MCA

- Work program

# Text boxes

N