| Plenary | Doc. ECC(14)015 |
| --- | --- |
| 36th Meeting |  |
| Cluj-Napoca, 11th – 14th March 2014 |  |
| Date issued: | 3rd March 2014 |
| Source: | Austria |
| Subject: | Comments on Draft Interim CEPT Report on 5 GHz |
| Group membership required to read? (Y/N) |
| Summary: |
| Bearing in mind the still existing interferences from WAS/RLANs to several radar systems (mainly weather radars) in the 5.6 GHz band and that the on-going work on 5 GHz WAS/RLAN extension is somehow foiling other European decisions already in force, Austria points out the necessity to protect incumbent services in these extension bands. Especially, it is crucial to safeguard ITS and TTT systems as well as the investments in the European Earth Observation Programme “Copernicus”. Austria recalls the pan-European plans to spread ITS including life-saving services in the 5.9 GHz band and the fact that many CEPT countries rely on a DSRC road tolling system in the 5.8 GHz band. As well the impending launch of the first satellite (Sentinel-1) of the above mentioned European GMES “Copernicus” requires a long-term strategy to guarantee appropriate protection of the 5.4 GHz band. Taking into account the preliminary results of sharing and compatibility analysis, which clearly indicate that there is no compatibility with ITS and TTT using these parameters, Austria reiterates its concerns to extend the band for WAS/RLANs too quickly and without further in-depth discussions. |
| Proposal: |
| The Austrian Administration requests ECC to -) take into account the proposed changes and comments within the document (Annex 1) -) consider the letter from ASD‐Eurospace on Copernicus/GMES (Annex 2) -) clarify the discrepancy between the assumed characteristics (1 W e.i.r.p. in paragraph 3.3) and the chosen characteristics (200 mW e.i.r.p. in paragraph 4.2) for the band 5725 - 5925 MHz -) refrain from an allocation for WAS/RLANs in 5350 - 5470 MHz and above 5725 MHz and/or foster a case by case individual authorisation instead of general authorisation or introduce other mitigation techniques, which fulfil protection requirements, and/or adopt the technical parameters in a way, that protection can be achieved and reflect the situation of these preliminary results in the chapters initial assessment and results |
| Background: |
| The Draft Interim Report from the WG FM Correspondence Group on 5 GHz WAS/RLANs was uploaded just 2 working days before the start of the last WGFM meeting. Therefore, it was not possible for Austria to prepare an input document on this issue for the WGFM meeting. Within the Drafting Group during the last WGFM meeting only the open questions as well as the input documents concerning the Draft Interim Report have been handled. |

# Text boxes

N