STG(14)24

| STG #38 WGSE - SEAMCAT Technical Group Copenhagen, ECO 7-8 April 2014 |  |
| --- | --- |
| Date Issued: 4 April 2014 Source : ECO Subject: feedback from testing of version alpha 5 |
| Document: for discussion/for information/for action |
| Password protection required? (Y/N) | N |

Summary: Feedback from testers on the alpha 5 has been gathered since the release

Proposal: STG to consider the feedback and to provide guidance

Background: Version Alpha 5 has been released to consider the mixed scenario and LTE power control as a request from STG(14)05 from EBU/TDF

- Mismatch of plugin from local jpk alpha 5 and distribution alpha 5 (Ticket #1172)

- Antenna pattern BS range [0,360] reset

- Propagation model P1546 migration rule buggy

- Slower than the version 4.1.0 - Memory issue – need for optimization

It turns out the AbstractDmaLink is created 1140 * 57 times, because it generates links from all users to all base stations. We had 57*20 users so 57*20*57 links. If these links were too heavy it causes slowdown.

There is probably more of this sort (and definitely at this moment because we are in limo between two models).

Running a 10 sample is done in 9 sec. (10 sec before). A 50 sample runs in 38 sec (41 with the slow code). It's better but still slow.

Besides the space issue, the algorithm could be improved a lot: we calculate connections and effective path loss to ALL base station. That sounds crazy as the distance to the BS grows you would expect the path loss to get bigger as well.