## Slide 1: Introduction to SEAMCAT
European Communications Office
Jean-Philippe Kermoal - SEAMCAT Manager (ECO)
3 June 2014
(Jean-Philippe.Kermoal@eco.cept.org)
EUROPEAN COMMUNICATIONS OFFICE | Nansensgade 19 DK-1366 Copenhagen Denmark | Telephone: + 45 33 89 63 00 Telefax: + 45 33 89 63 30 | E-mail: eco@eco.cept.org Web Site: http://www.cept.org/eco

## Slide 2: Outline
Spectrum Engineering
SEAMCAT
Conclusions

## Slide 3: Spectrum engineering challenges
The requirement for global compatibility amongst many radio systems within a congested radio spectrum
introduction of new radio applications
technological
regulatory
economic considerations
increasing penetration of the existing radio applications

## Slide 4
There are no more “empty” spectrum
Proposed new systems have to find way of “sharing” with some of existing systems
Thus the need for spectrum engineering and optimisation:
  to find which existing radio systems are easiest to share with, and then
  determine the “sharing rules”
Need for spectrum sharing

## Slide 5
Spacing radio systems in frequency
  Using the gaps between existing channels
Spacing geographically
  Using the gaps between intended deployment areas (e.g. cities vs. rural areas)
Time sharing
  Exploiting different work time (day vs. night)
Working at different power levels
  E.g. “underlay” spectrum use by UWB
Sharing methods

## Slide 6
Agile (cognitive) radio systems require minimum sharing rules as they could be adapting dynamically
  Simple example: finding free channel in a given geographic area
Traditional rigid-design radio system will require precisely defined sharing rules
  Maximum transmit power, guard-bands to existing systems, etc
Sharing implementation

## Slide 7
Analytical analysis, usually by worst-case approach:
  Minimum Coupling Loss (MCL) method, to establish rigid rules for minimum “separation”
Statistical analysis of random trials:
  The Monte-Carlo method, to establish probability of interference for a given realistic deployment scenario
  That is where SEAMCAT comes into picture!
Defining the sharing rules

## Slide 8: Strategic tool for CEPT
For performing compatibility/sharing studies
  Used in generating studies for ECC/CEPT Reports
As a Reference tool
  Recognised at ITU (Rep. ITU-R SM.2028-1)
As an agreed work platform
  Project Teams (PTs) can focus on the input parameters and not on the algorithm
  Sharing simulation between proponents ease the trust in the results
For educating future generation of spectrum engineer (Administrations, Industry or University)

## Slide 9: Usage in and outside CEPT
Source: google analytics on the www.seamcat.org download page in 2012.
2012 survey: about 1000 people downloaded SEAMCAT.

## Slide 10: SEAMCAT-4 Software tool
SEAMCAT is not a CAT

## Slide 11: History
Developed in CEPT as a co-operation between National Regulatory Administrations, ECO and industry
First released in Jan-2000, then gradually developed in several phases
Latest version 4.1.0 (October 2013)
Freely downloadable from ECO website (www.seamcat.org)

## Slide 12
SEAMCAT is designed for:
  Co-existence studies between different radio systems operating in same or adjacent frequency bands
  Any type of radio systems in terrestrial scenarios
  Extended to cellular system like CDMA and OFDMA
  Quantification of probability of interference between various radio systems
Not designed for system planning purposes
Based on Monte-Carlo generation
Purpose

## Slide 13
Mobile:
  Land Mobile Systems
  Short Range Devices
  Earth based components of satellite systems
Broadcasting:
  terrestrial systems
  DTH receivers of satellite systems
Fixed:
  Point-to-Point and Point-to-Multipoint
  ... and more
Typical examples of modelled system

## Slide 14
Installing SEAMCAT
(administrative right needed)
On-line Webstart:
Internet connection is needed at least for the installation; during later runs Internet used (if available) to check for updated version
Off-line
(Windows, Linux, Mac)
(Windows only)
1GB RAM needed
Java Runtime Environment (RTE) (version 1.6._027 and above)

## Slide 15
Installing SEAMCAT
(without administrative right)
Off-line only using a USB stick
(Windows only)
http://tractool.seamcat.org/wiki/Manual/Introduction/Installing#Withoutadministrativeright

## Slide 16
Files installation

## Slide 17: Conclusions
Sharing rules are important element of spectrum optimisation process
Unless some intelligent interference avoidance is implemented in radio systems, the careful choice of sharing conditions is the only means for achieving successful co-existence and optimal spectrum use
Statistical tool SEAMCAT is a powerful tool for such analysis
Strategic tool for the CEPT
Reference tool – recognised at ITU
World wide usage
Free tool to run on any operating system platform

## Slide 18: Thank you - Any questions?