## Slide 1: Setting Emission and Blocking masks
European Communications Office
Jean-Philippe Kermoal (ECO)
3 June 2014
EUROPEAN COMMUNICATIONS OFFICE | Nansensgade 19 DK-1366 Copenhagen Denmark | Telephone: + 45 33 89 63 00 Telefax: + 45 33 89 63 30 | E-mail: eco@eco.cept.org Web Site: http://www.cept.org/eco

## Slide 2: Outline
Using library
ACLR
Emission Mask
OFDMA example
Blocking Mask / ACS
Exercise #1
Emission floor

## Slide 3: Using Library
Edit
Import from library
Export to library
Edit
Import
Export
Technical specifications commonly extracted from ETSI (see http://www.etsi.org/WebSite/Standards/Standard.aspx)

## Slide 4: Editing the mask
The emission mask defaults value
Remove the default using the Clear button.
Then use the add button to add the enough blank rows for half of the emission mask.
Note the format of the data:
  Offset = MHz
  Unwanted = dBc
  Reference bandwidth = kHz

## Slide 5: Symmetry
Then use the Sym button to get a symetric mask

## Slide 6: Reference/normalised bandwidth
Once SEAMCAT has generated the whole mask, first check that the values are in the correct order.
The unwanted emission diagram shows two masks
The red mask is the representation using the user defined reference bandwidth.
The blue mask is normalised to 1MHz measurement bandwidth.
The user may normalise his input to 1MHz bandwidth but it can be useful to input the mask in the bandwidth defined in the standard and allow SEAMCAT to create normalised mask.

## Slide 7: Store your mask on disk
Spectrum mask can be saved as .txt file
it can be reused for other workspaces using load buttons.

## Slide 8: General
Ref. BW 10 KHz
Emission BW = Ref. BW = 20 KHz
System with 30 dBm in a emission bandwidth of 20 KHz

## Slide 9: OFDMA emission mask - UE example
SEAMCAT calculates the absolute unwanted power in taking account of the bandwidth of the VLR and the Ref. BW defined with the mask by integrating the relative power and considering then the total transmitted power.
In case the limits are given as absolute power in dBm (as with this example) the values of the Mask are given by the difference of the limit and the total power, e.g. -15 dBm -23 dBm = -38 dBc

## Slide 10: Exercise #1 – edit a Mask in the library
On the next step make the mask symmetrical
“Close” saves also the actual status

## Slide 11: Emission Floor
This emission floor mask (frequency offset (MHz), emission floor (dBm), reference bandwidth (MHz)).
Useful when power control is used

## Slide 12: ACIR = f(ACLR, ACS)
ACIR = adjacent-channel interference ratio
In UL, the dominant part of ACIR is due to the UE adjacent channel leakage (ACLR) i.e. ACSBS is very large compare to ACLRUE and ACIR ≈ ACLRUE.
In DL, the dominant part of ACIR is due to the UE frequency selectivity (ACS) i.e. ACLRBS is very large compare to ACSUE and ACIR ≈ ACSUE
No use of the ACLR value directly. Emission spectrum Mask is used

## Slide 13: Blocking Mask (generic)
User-defined mode
Protection ratio
Sensitivity modes
fv
Receiver Mask
fI
Rx bandwidth
Rejection
of the receiver
ACS
(ETSI)
Blocking
(ETSI)
+
Blocking:
Blocking Response =
(PR and Sensitivity mode)
fv
Receiver Mask
fI
Rx bandwidth
Rejection
of the receiver
Blocking Response = filtering (user defined mode)
Blocking:

## Slide 14: CDMA and OFDMA ACS
ACS is the same as the blocking attenuation input

## Slide 15: OFDMA BS blocking Mask example
Extract from CEPT Report 40 (ITU-R Report M2039)

## Slide 16: Thank you - Any Questions?