## Slide 1: Overview of Systems in SEAMCAT
European Communications Office
Jean-Philippe Kermoal - SEAMCAT Manager (ECO)
3 June 2014
(Jean-Philippe.Kermoal@eco.cept.org)
EUROPEAN COMMUNICATIONS OFFICE | Nansensgade 19 DK-1366 Copenhagen Denmark | Telephone: + 45 33 89 63 00 Telefax: + 45 33 89 63 30 | E-mail: eco@eco.cpet.org Web Site: http://www.cept.org/eco

## Slide 2: Outline
Cellular system … in brief
System type
Conclusion
Simple interface
”Generic” system

## Slide 3: System type
Generic
CDMA
OFDMA

## Slide 4: Generic system
Start
While i=1,N
Generate position data of VLT, VLR
Calculate dRSSi
dRSS vector
While i=1,N
Generate position data of ILTj, ILRj
Calculate iRSSi,j
iRSS vector
While j=1,M
Calculate iRSSiSUM
dRSS, iRSS to ICE
A
B
C
D

## Slide 5: Simple and harmonised interface
Add
Duplicate
Delete
Multiple interferer generation
On-line Help
Workspaces
Interfering links

## Slide 6: Cellular modelling
Modelling of cellular systems as victim, interferer, or both:
  Quasi-static time within a snapshot
  One direction at a time (uplink or downlink)
CDMA
  Voice traffic only
  Particular CDMA standard defined by setting Link Level Data (CDMA2000-1X, W-CDMA/UMTS)
OFDMA
  LTE

## Slide 7: CDMA system modelling
First a succession of snapshots are run without interference, gradually loading the system to find the target non-interfered capacity per cell
apply interference and note the impact in terms of how many of initial users were disconnected
Generate position data of Wtj, Vrj
While j=1, L
Iterative process of power balancing in CDMA cells
Record dRSSi or other parameter, e.g. non-interfered CDMA capacity
Start
While i=1, N
Generate position data of Itk, Wrk
Calculate iRSSi,k
While k=1, M
Repeat iterative process of power balancing in victim CDMA cells, now with iRSS present as external impact
(N) records of interference impact
Record impacti of interference, e.g. loss of CDMA capacity
To further engines
CDMA as victim
Generate position data of Itj, Wrj
C
D
While j=1, M
Iterative process of power balancing in CDMA cells
Calculate iRSSi,j
While j=1, M
CDMA as
interferer

## Slide 8: CDMA vs OFDMA simulation
CDMA
CDMA performs a power tuning process when surrounded by two tiers of auxiliary cells, and total cluster of 19.
OFDMA
OFDMA performs an iterative process of assigning a variable number of traffic sub-carriers and calculating the overall carried traffic per base station.
OFDMA systems similar to CDMA systems
Except: After the overall two-tiers cellular system structure (incl. wrap-around) is built and populated with mobiles

## Slide 9: Conclusions
Harmonised interface between generic and CDMA/OFDMA modules
Versatile tool to configure victim and interferer

## Slide 10: Thank you - Any questions?