## Slide 1: Basic functionality: coverage/simulation radius
European Communications Office
Jean-Philippe Kermoal (ECO)
05 June 2012
EUROPEAN COMMUNICATIONS OFFICE | Nansensgade 19 DK-1366 Copenhagen Denmark | Telephone: + 45 33 89 63 00 Telefax: + 45 33 89 63 30 | E-mail: eco@eco.cept.org Web Site: http://www.cept.org/eco

## Slide 2: Outline
dRSS calculation
Probability of interference
Interference contribution
Exercise #6 – Coverage radius
iRSS calculation
Exercise #7 – Simulation Radius
Exercise #8

## Slide 3: dRSS calculation
Define Victim Link Receiver (VLR)
Operating frequency
Receiver bandwidth
Antenna Characteristics
Interference criteria
Noise floor
Define Victim Link Transmitter (VLT)
Tx power
Antenna characteristics
Position the VLR to VLT
(Coverage Radius)
You will learn how to ...
Calculate the dRSS
Test propagation model
Launch simulation
Extract dRSS vectors
✓
✓
✓
✓
✓
✓
✓

## Slide 4: SEAMCAT scenario

## Slide 5: Exercise #6 - dRSS

## Slide 6: Victim Link Receiver

## Slide 7: Victim Link Transmitter
VLT and VLR pointing at each other

## Slide 8: Position of the VLR to VLT (1/2)
Uncorrelated mode
User-defined Radius
Correlated mode
Correlated distance (origin = VLT)
Noise limited Network
Traffic limited Network
VLT ↔ VLR
location
Coverage radius

## Slide 9: Position of the VLR to VLT (2/2)
Victim Link
Transmitter
(VLT)
Victim Link
Receiver
(VLR)
dRSS
Victim link
(0,0)
(2 km,2 km)
Delta X = 2 km
Delta Y = 2 km
x
y

## Slide 10: Calculation of the Path loss
L = 32.44+10log(8)+20log(1000))
L = 101.47 dB

## Slide 11: Calculation of dRSS
dRSS = Pe+Ge+Gr-L
dRSS = 30(dBm)+9 (dBi)+9 (dBi)-101.47 (dB)
dRSS = -53.47dBm

## Slide 12: Extract dRSS
Only for uncorrelated mode

## Slide 13: Coverage Radius (Position of the VLR to VLT) and (Position of the ILR to ILT)

## Slide 14: iRSS calculation
You will learn how to ...
Position the VLR vs ILT (Simulation Radius)
✓
Calculate the iRSS
✓
Define Interfering Link Transmitter (ILT)
Tx power
Antenna Characteristics
Set the emission bandwidth
✓

## Slide 15: SEAMCAT scenario

## Slide 16: Exercise #7 - iRSS

## Slide 17: Interfering Frequency

## Slide 18: Position of the Vr vr It (1/2)
Uncorrelated mode
None
(nactive interferers)
ILT /VLR
Correlated mode
ILT /VLT
ILR /VLR
ILR/VLT
Uniform density (nactive interferers)
Closest
(single interferer)
VLR ↔ ILT
location
Simulation radius

## Slide 19: Position of the VLR vr ILR (2/2)
Victim
Link Receiver
(VLR)
Interfering Link
Receiver
(ILR)
Interfering Link
Transmitter
(ILT)
Victim link
Transmitter
(VLT)
dRSS
iRSS
Victim link
Interfering link
Delta X = 4 km
Delta Y
= 4 km

## Slide 20: Calculation of the iRSS
iRSS = Pe+Ge+Gr-L
iRSS = 33(dBm)+11 (dBi)+9 (dBi)-(32.5+10log(32)+20log(1000))
iRSS = -54.5dBm
P(dBm/Bref) = Pe (dBm)+Att(dBc/Bref)
33 (dBm/200KHz) = 33 + 0 (dBc/Bref)

## Slide 21: Simulation Radius (Position of the VLR to ILT)

## Slide 22: Probability of interference
You will learn how to ...
Compatibility calculation mode
✓
Extract the Probability of Interference in ....
✓
Translation calculation mode
✓

## Slide 23: Probability of interference
  Calculation mode: compatibility or translation
  Which type of interference signal is considered for calculation: unwanted, blocking, intermodulation or their combination
  Interference criterion: C/I, C/(N+I), (N+I)/N or I/N

## Slide 24: Compatibility calculation mode
the C/I (i.e. dRSS/iRSS) can be derived:
  dRSS/iRSS = -53.5-(-54.5) = 1dB
Make sure that dRSS>sensitivity

## Slide 25: Translation calculation mode
Low interfering Tx power results in no interference (p=0%)
Gradual increasein the ILT power results in increasing P%
ILT power is high enough to results in 100%

## Slide 26: Interference contribution
You will learn how to ...
Calculate the iRSS unwanted
✓
Calculate the iRSS blocking
user-defined mode
Sensitivity mode
Protection ratio mode
✓
Extract probability of interference
(i.e. unwanted vs blocking)
✓
Modify the Unwanted Emission Mask
✓

## Slide 27: Exercise #8
P = 33 +(–23(dBc/Bref)) = 10 (dBm/200kHz)
Change the ILT frequency to 1000.3 MHz
Change the SEM as follow:

## Slide 28: Calculate iRSS unwanted
iRSS unwanted calculate the interfering power received by the Victim receiver within its bandwidth
In this example there is no bandwidth correction factor to be applied to the calculation of the iRSS unwanted since the Vr bandwidth and the It reference bandwidth have the same value (i.e. 200 KHz).
Unwanted:
fVr
fIt
Interfering
emission mask
Rx bandwidth
iRSSunwanted = P+Ge+Gr-L
iRSSunwanted = 10(dBm/200kHz)+11+9-(32.5+10log(32)+20log(1000))
iRSSunwanted = -77.5dBm

## Slide 29: Calculate iRSS blocking (1/4)
Change the blocking mask as follow:
fVLR
fILT

## Slide 30: Calculate iRSS blocking (2/4)
User-defined mode:
  iRSS blocking (fit) = Pe+Ge+Gr-L-Att (fit)
  iRSS blocking = 33(dBm)+11+9-(32.5+10log(32)+20log(1000))-40(dB)
  iRSS blocking = -94.5dBm
The It bandwidth is not considered in the iRSS blocking calculation)
Blocking:
fVr
Receiver Mask
fIt
Rx bandwidth
Rejection
of the receiver

## Slide 31: Calculate iRSS blocking (3/4)
Sensitivity mode:
  Attenuation(f) = block(f) [dBm] – sensvr [dBm] + C/(N+I) [dB]
  Sensitivity = Noise Floor + C/(N+I)
  Sensitivity = -110dBm + 16
  = -94dBm
  Attenuation (f ) = 40-(-94)+16= 150dB
  iRSS blocking (fit) = Pe+Ge+Gr-L-Att (fit)
  iRSS blocking = -54.5-150
  = -204.5dBm

## Slide 32: Calculate iRSS blocking (4/4)
Protection Ratio:
  Attenuation(f) = block(f) [dBm] + C/(N+I) [dB] + 3dB
  Attenuation(f) = 40 +16 +3 = 59 dB
  iRSS blocking (fit) = Pe+Ge+Gr-L-Att (fit)
  iRSS blocking = -54.5-59
  = -113.5 dBm

## Slide 33: Probability of interference (1/2)
For the unwanted mode, the C/I can be derived as:
  dRSS/iRSS unwanted = -53.5-(-77.5) = 24dB
Since the resulting C/I is above the protection criteria (19 dB), the probability of interference is 0
It is also possible to derive the (N+I)/N= -77.5-(-100)= 22.5 (since I>>N). Since the (I+N)/N which is obtained is above the protection criteria (3dB), the probability of interference is 1

## Slide 34: Probability of interference (2/2)
For the blocking mode, the C/I can be derived as:
  dRSS/iRSS blocking = -53.5-(-113.5) = 60dB
Since the resulting C/I is above the protection criteria (19 dB), the probability of interference is 0
It is also possible to derive the (N+I)/N= -113.5-(-100)= -13.5. Since the (I+N)/N which is obtained is below the protection criteria (3dB), the probability of interference is 0

## Slide 35: Thank you - Any Questions?