ECC PT1(12)046 Annex 20

| To: Mr Jean Philippe Kermoal Chairman STG jean-philippe.kermoal@eco.cept.org C.c. Chairman WGSE Mr Bruno Espinosa (espinosa@anfr.fr) |  |  |
| --- | --- | --- |
|  | Date: 14th April 2012 |
| Source: ECC PT1 |
| Subject: SEAMCAT enhancements |

Dear Jean-Philippe,

ECC PT1 has discussed and analysed the input document from ECO < Review of some SEAMCAT feature useful for ECC PT1>, and would like to provide the following comments and proposal on the way-forward:

- Interference calculation

- For the adjacent band compatibility, the interference calculation method in Seamcat is correct when both interfering and victim system have the same channel bandwidth. For the case of different channel bandwidths of interfering and victim systems, it might be useful to further check the bandwidth conversion in the calculation of ACLR and ACS.

- For the co-channel compatibility simulation, there may be a problem of interference calculation, the detailed analysis can be found in the attached document ECC-PT1(12)040.

- New features list for PT1’s work

- Propagation model for 3.4-3.8 GHz frequency band. ECC-PT1 is working on the appropriate propagation model for 3.5 GHz band, once this work is completed, ECC-PT1 will ask ECO to implement one or several new propagation models for the technical studies on 3.4-3.8 GHz band technical conditions.

- ECC-PT1 plans to study the co-existence for different types of base stations: macrocell, microcell, and femtocell in 3.4-3.8 GHz band, the implementation of a Manhattan microcell configuration in Seamcat is needed, the implementation of indoor femtocell configuration is also needed, 3GPP RAN_4 has done a lot of indoor co-existence simulations when developing the home BS technical specification, the indoor simulation method used by 3GPP can be considered.

- A cellular network structure in generic system module will be very useful for the simulations of non CDMA/OFDM systems, such as GSM. The expected output can be the distribution (probability) of C/I and/or C/(I+N)

- Aggregated field strength distribution from all the base stations at borderline with distance D from the reference cell base station, as shown in figure 1 below. This is needed in the work of border coordination simulation work for determining the trigger values for border coordination.

Figure 1: Aggregated field strength distribution at borderline

- Proposed way-forward

ECC-PT1 would like to propose to create a correspondence group through ECO Forum on Seamcat enhancement. It is proposed that this group can be lead by ECO inviting technical experts from ECC-PT1, STG, and WG SE, the tasks are

- Further validation on the interference calculation method, and develop a co-channel interference calculation method specification;

- Develop the technical specifications of the new features listed above.

It is noted that WGSE may have other requirements for example the work within SE40 (see LS from PT1 to SE40 where some issues with SEAMCAT were highlighted).

Best regards,

Didier Chauveau

Chairman CEPT ECC PT1

Chauveau@anfr.fr

# Text boxes

Network A

Borderline

D