STG(12)21

| To: Mr Jean Philippe Kermoal Chairman STG jean-philippe.kermoal@eco.cept.org C.c. : Acting Chairmen WGSE Mr. Karl Loew (karl.loew@bnetza.de) Mr. Alexandre Kholod (alexandre.kholod@bakom.admin.ch) |  |  |
| --- | --- | --- |
|  | Date: 19th September 2012 |
| Source: ECC PT1 |
| Subject: Guidance on possible SEAMCAT update |

Dear Jean-Philippe,

In its last meeting (17-22 September 2012), ECC PT1 reviewed the LS from STG and provides the following guidance:

Use of voice activity factor in SEAMCATCDMA uplink simulations

ECC PT1 recommends to set the activity factor to 1 and to therefore remove inactive users from the algorithm to reduce computer power for both UL and DL. Consequently, it is proposed to remove also the “voice activity factor” input from the interface. The end results should be as follow so that the term “active users” is reflected

Ex: capacity loss: 10 % of active users dropped.

Target cell noise rise of the enhanced CDMA uplink algorithm

ECC PT1 recommends changing the default input value from 0.8 to 0.01 dB. This will results in the algorithm to consider all the cells in the network to be considered in the noise rise compensation if the user does not change the default value while leaving the freedom to a user to choose another value. The value of 0.01 dB has been chosen to ensure that the analysis does not disregard any cases of lost calls, since calls may be dropped even for very low noise rise levels.

Interference Calculation for CDMA and OFDMA module

ECC PT1 considered the issue of the calculation of the interference from external interferer for the CDMA and OFDMA module (see Annex 1). It was found out from a LS of ECC PT1 of its previous meeting that when the victim BW and interfering BW overlap the blocking calculation may need to be modify. In addition it was identified that the co-channel case the inclusion of blocking value was not appropriate as the Tx power is counted twice.

ECC PT1 proposes that the interference be calculated using the following generic formula:

I total = Unwanted + Blocking

Where Unwanted = TxP – Pathloss1 + Gtx + Grx – ACLR

ACLR is the integrated energy over the all victim Rx bandwidth (i.e. no change)

Where Blocking = (α+β)TxP – Pathloss1 + Gtx + Grx – ACS

(α+β) = 1 for adjacent channel and (α+β)=0 for cochannel scenario (i.e. changed proposed)

(α+β) is a ratio based on the amount of victim BW overlapping with interfering BW. Note that this ratio should be applied to the linear domain.

This also means that there would be a need to add a new input field for the interfering bandwidth.

Propagation model for 3.4-3.8 GHz frequency band

ECC PT1 expects to use existing build-in model or develop its own plugin. There is no further request on this topic for STG. There is no need for assistance from the 2013 budget.

Manhattan microcell configuration

Currently there is no Manhattan microcell model source code available for STG. ECC PT1 will need to assess the need and the urgency for such a model in SEAMCAT for studies that ECC PT1 may undertake in the future.

For the time being STG does not need to progress with this item and can therefore remove it from its work program.

Generic system

ECC PT1 would like to propose the initial guidance for the drafting of the specification for the generic system:

- Frequency re-use pattern: ECC PT1 recommends to use not only fix pattern (BCCH-12), but also to allow simulate frequency hopping. ECC PT1 would prefer to have SEAMCAT to compute it automatically. ECC PT1 proposes 2 steps:

Step 1: Cellular structure as general module and user introduce frequency plan. Consider the possibility to upload an xls format frequency plan or create a default template for the frequency (may be consider an extra “user-defined” in the distribution panel).

Step 2: after reception of the specification for the frequency re-use pattern and frequency hopping.

- Power control: ECC PT1 recommends to use the generic model approach

- C/I: ECC PT1 reminded that for one event only one UE (within a time frame) is connected to a BS within a cell. Therefore ECC PT1 recommend to have a ref cell C/I vector (1xnumber_events) and a system cell C/I vector (1 x (number_sites x number_events)

- Outage measure: Percentage of C/I above a 6, 9, 12 dB that is used as measure of interference.  Add an input parameter Target C/I_user defined (dB).

Proposal of output results:

-	C/I vectors (ref cell + system)

-	Reference cell:

(Target C/I_user defined) dB           x%

-	Generic system:

(Target C/I_user defined) dB           x%

- Deadline: Good to have it. Too late for 2012 budget, but could be useful in future work. No time pressure.

Aggregated field strength

ECC PT1 noted the proposed solution. There is no further action needed from STG on this issue.

ITU-R F1336 antenna pattern for the SEAMCAT library

In addition, ECC PT1 is considering BS antenna patterns for its 3.4-3.8 GHz band Macrocell study and agreed to use, for compatibility studies, the BS antenna defined in ITU-R F.1336 with a 17 dBi antenna gain as shown in figure below.

ECC PT1 invites STG to add these antenna patterns into the SEAMCAT library. The enclosed BS antenna patterns are derived from ITU-R F1336-3 using the average side-lobe patterns formula (section 3.2) with maximum antenna gain of 17 dBi and k=0.2 for involving typical antennas.

| Horizontal pattern | Vertical pattern |
| --- | --- |

Attached antenna pattern:

SEAMCAT workshop

There was interest expressed during the ECC PT1 to have a workshop on SEAMCAT. ECO is to investigate the possibility to organize it.

Best regards,

Didier Chauveau

Chairman CEPT ECC PT1

Chauveau@anfr.fr

Annex 1

Interference Calculation for CDMA and OFDMA module