## Slide 1: Introduction to SEAMCAT
European Communications Office
Jean-Philippe Kermoal - SEAMCAT Manager (ECO)
27 November 2012
(Jean-Philippe.Kermoal@eco.cept.org)
EUROPEAN COMMUNICATIONS OFFICE | Nansensgade 19 DK-1366 Copenhagen Denmark | Telephone: + 45 33 89 63 00 Telefax: + 45 33 89 63 30 | E-mail: eco@eco.cept.org Web Site: http://www.cept.org/eco

## Slide 2: Outline
Why SEAMCAT?
SEAMCAT-4 software tool
Conclusions

## Slide 3: Part 1: Why SEAMCAT?

## Slide 4: Spectrum engineering challenges
The requirement for global compatibility amongst many radio systems within a congested radio spectrum
introduction of new radio applications
technological
regulatory
economic considerations
increasing penetration of the existing radio applications

## Slide 5
There are no more “empty” spectrum
Proposed new systems have to find way of “sharing” with some of existing systems
Thus the need for spectrum engineering and optimisation:
  to find which existing radio systems are easiest to share with, and then
  determine the “sharing rules”
Need for spectrum sharing

## Slide 6
Spacing radio systems in frequency
  Using the gaps between existing channels
Spacing geographically
  Using the gaps between intended deployment areas (e.g. cities vs. rural areas)
Time sharing
  Exploiting different work time (day vs. night)
Working at different power levels
  E.g. “underlay” spectrum use by UWB
Sharing methods

## Slide 7
Agile (cognitive) radio systems require minimum sharing rules as they could be adapting dynamically
  Simple example: finding free channel in a given geographic area
Traditional rigid-design radio system will require precisely defined sharing rules
  Maximum transmit power, guard-bands to existing systems, etc
Sharing implementation

## Slide 8
Analytical analysis, usually by worst-case approach:
  Minimum Coupling Loss (MCL) method, to establish rigid rules for minimum “separation”
Statistical analysis of random trials:
  The Monte-Carlo method, to establish probability of interference for a given realistic deployment scenario
  That is where SEAMCAT comes into picture!
Defining the sharing rules

## Slide 9: Strategic tool for CEPT
For performing compatibility/sharing studies
  Used in generating studies for ECC/CEPT Reports
As a Reference tool
  Recognised at ITU (Rep. ITU-R SM.2028-1)
As an agreed work platform
  Project Teams (PTs) can focus on the input parameters and not on the algorithm
  Sharing simulation between proponents ease the trust in the results
For educating future generation of spectrum engineer (Administrations, Industry or University)

## Slide 10: Usage within and outside CEPT
Source: google analytics on the www.seamcat.org download page (May 2011/2012 period)

## Slide 11: Part 2: SEAMCAT-4 Software tool

## Slide 13: History
Developed in CEPT as a co-operation between National Regulatory Administrations, ECO, industry
First released in Jan-2000, then gradually developed in several phases
Latest version 4.0.0 (May 2012)
Freely downloadable from ECO website (www.seamcat.org)

## Slide 14
SEAMCAT is designed for:
  Generic co-existence studies between different radiocommunications systems operating in same or adjacent frequency bands
  Extended to cellular system like CDMA and OFDMA
  Evaluation of transmitter and receiver masks
  Evaluation of various limits:
    unwanted emissions (spurious and out-of-band),
    blocking/selectivity, etc.
Not designed for system planning purposes
Purpose

## Slide 15: SEAMCAT tool
Used for analysis of a variety of radio compatibility scenarios:
  quantification of probability of interference between various radio systems
  consideration of spatial and temporal distributions of the received signals
Can model any type of radio systems in terrestrial interference scenarios
Based on Monte-Carlo generation

## Slide 16
Mobile:
  Land Mobile Systems
  Short Range Devices
  Earth based components of satellite systems
Broadcasting:
  terrestrial systems
  DTH receivers of satellite systems
Fixed:
  Point-to-Point and Point-to-Multipoint
  ... and more
Typical examples of modelled system

## Slide 17
Installing SEAMCAT
(administrative right needed)
On-line Webstart:
Internet connection is needed at least for the installation; during later runs Internet used (if available) to check for updated version
Off-line
(Windows, Linux, Mac)
(Windows only)
1GB RAM needed
Java Runtime Environment (RTE) (version 1.6._027 and above)

## Slide 18
Installing SEAMCAT
(without administrative right)
Off-line only using a USB stick
(Windows only)
http://tractool.seamcat.org/wiki/Manual/Introduction/Installing#Withoutadministrativeright

## Slide 19
Files installation

## Slide 20
Source code
Open source in Java
Source code available upon request
2 steps procedure:
  License agreement to sign
  Register to the “seamcat source code” group

## Slide 21
Software architecture
Technical Library (masks, antenna etc..)
Workspace (.sws)
Results
XML File
Event Generation Engine
EGE results display (generic)
CDMA Engine
Interference Calculation Engine
CDMA results display
OFDMA results display
User Interface
Plug-ins (propagation model etc..)
Reports
XML stylesheets
OFDMA Engine
ICE results display
input parameters

## Slide 22
Windows-oriented
Main element – workspace.sws
Main interface
Simulations input data – scenario:
Equipment parameters, placement, propagations settings, etc.
Simulation controls:
number of events etc..
Simulation results:
dRSS/iRSS vectors, Pinterference, Cellular structure

## Slide 23
Data exchange via XML
Physically a .zip file with “sws” extension including XML files for the scenario and the results

## Slide 24: SEAMCAT-4 software
Based on SEAMCAT-3 (early 2003) and SEAMCAT-2 workspace based, dialogue views
Main reason: drastic graphical interface change to ease:
  The access to input parameters
  The comparison of workspace
  The use of libraries
  The use of batch

## Slide 25: Graphic interface (1/1)
Easy view of parameters at a glance
Easy comparison of workpsaces
Graphical reminders (tooltip)

## Slide 26: Graphic interface (1/2)
Shows positions and budget link information of the victim and interfering systems
Overview of results (dRSS, iRSS)
Intuitive check of simulation scenario

## Slide 27: Libraries and Batch
Easy to create workspaces with predefined libraries
  Edit, import, export
Easy to run sequentially workspaces
  Batch operation
  Intuitive use

## Slide 28: Extra features
History + welcome
Propagation model plug-in API(Application Programing Interface)
Post processing plug-in API
Custom simulation report (XSLT->XML style sheet)
Multiple vector display
Propagation model compare tool

## Slide 29: Welcome + News History
Welcome + News
History

## Slide 30
A plug-in is a (little) software programme, which may be developed by YOU
  Written using standard Java language, compiled using open development tools
  The pre-compiled code may be then “plugged-in” at certain “insertion points” of SEAMCAT simulation flow to produce the desired “user-defined” functionality
No perceivable impact on simulation speed
Can be embedded to the workspace for sharing with others
Plug-in

## Slide 31
This plug-in may be used to define ANY kind of propagation model
The plug-in may be inserted at any point where propagation model is defined in the scenario
Propagation model plug-in
  No complexity limit
  No limit to the inputs
  Description of inputs

## Slide 32
This plug-in is invoked at the end of the snapshot generation and may be used e.g.:
  Powerful API
  Introduce user-defined consistency checks
  Model some special system design features, e.g. Smart Antennas, etc.
  Account for any additional environment features, e.g. terrain/clutter impact, etc
  To save intermediate results into external files for signal processing in other tools (Matlab, etc)
  not applicable to CDMA (victim)
Post-processing plug-in

## Slide 33
Predefined (html, xls..)
Custom style sheet
Simulation report

## Slide 34
Multiple vectors display
Calculated vectors or external vectors
Statistics and signal type

## Slide 35
Comparing propagation model
Compare two or more propagation models
Results in linear or log format

## Slide 36: Conclusions
Sharing rules are important element of spectrum optimisation process
Unless some intelligent interference avoidance is implemented in radio systems, the careful choice of sharing conditions is the only means for achieving successful co-existence and optimal spectrum use
Statistical tool SEAMCAT is a powerful tool for such analysis
Strategic tool for the CEPT
Reference tool – recognised at ITU
World wide usage

## Slide 37: Thank you - Any questions?