## Slide 1: Modeling of Unwanted and Blocking Interference Modes
European Communications Office
Jean-Philippe Kermoal
27 November 2012
EUROPEAN COMMUNICATIONS OFFICE | Nansensgade 19 DK-1366 Copenhagen Denmark | Telephone: + 45 33 89 63 00 Telefax: + 45 33 89 63 30 | E-mail: eco@eco.cpet.org Web Site: http://www.cept.org/eco

## Slide 2: Outline
Interfering modes
Blocking case
Unwanted emissions case
Exercise #2
Exercise #4
Exercise #3

## Slide 3: Interference Calculations
Interfering Modes
Interference Criteria
Unwanted and Blocking Signals

## Slide 4: Unwanted Emissions
Victim
fv
Receiver Bandwidth
Interfering System
fI
Interfering emission mask
fI
Interferer emission mask

## Slide 5: Exercise #2: Unwanted calculation
Set victim link receiver (VLR)
  Name: VLR Exercise #2
  Frequency: 910 MHz
  Interference criteria: I/N = 0
  Noise level = -110
  Bandwidth = 150 KHz
Set interfering link transmitter (ILT)
  Name: ILT Exercise #2
  Frequency: 905 MHz
  Power: 23 dBm
  Emission mask: default mask
Path between VLR with ILT
  Propagation model:free space (no variation)
  Position (x,y): fixed, 10km apart

## Slide 6: Victim link

## Slide 7: Victim Link Receiver
Interference criteria
Reception bandwidth
Description
Noise floor

## Slide 8: Interfering Link

## Slide 9: Interfering Link Transmitter
Power
Emission mask

## Slide 10: Unwanted emissions mask
Default value
erroneous value
See the following presentations...

## Slide 11: ILT  VLR Path
Att = 32.44 + 20 x log (f (MHz)) + 20 x log (d (km))
Att = 32.44 + 20 x log (905 MHz) + 20 x log (10 km)
Att = 111.57 dB

## Slide 12: Simulations...
10 km
IRSS Unwanted = Pe + Ge + Gr – Att (free space) IRSS Unwanted = 13.79 dBm + 0 dB + 0 dB – 111.57 dB IRSS Unwanted = - 97.78 dBm
Power in the victim bandwidth:
P(dBm/Bref) = Pe(dBm) + att(dBc/Bref) + CF
Pe = 23 dBm + 0 + 10*log(150/1250)
Pe = 23 dBm + 0 - 9.21dBm
Pe = 13.79 dBm
Correction Factor (CF) needed because Vr BW < It BW

## Slide 13: Results
N = -110 dBm IRSS Unwanted = - 97.78 dBm I/N = - 97.78 – (-110) = 12.21 dB ( Calculated by SEAMCAT) Interference Criterion was: I/N = 0 ( Input to SEAMCAT)

## Slide 14: Results...
I/N = 0 respected for Pe < 12.5 dB at 50%

## Slide 15: Exercise #3: SEM calculation
Easy tool in SEAMCAT  “Test Rel. unwanted” tool
  Launch the “Test Rel. unwanted” tool
  Df = fi-fv = 0
  Vr BW = 150 kHz
  SEM: same as in Exercise #2
  Results: __ dBm
How to check that the Spectrum Emission Mask is properly calculated?

## Slide 16: Blocking
Victim
fv
Receiver Bandwidth
Interfering System
fI
Interferer
fI
Rejection of the receiver

## Slide 17: Blocking: 3 Modes
User Defined (dB): Rejection at the receiver AttBlocking = BlockUD
Protection Ratio (dB): AttBlocking = BlockPR + C/(N+I) + 3 dB
Sensitivity Mode (dBm): Maximum Acceptable Value of Power AttBlocking = BlockSens (dBm) – Sensitivity (dBm) + C/(N+I)
A desensitisation (N+I/N) of 3 dB is assumed

## Slide 18: But not so different
Protection Ratio: Interfering Blocking Level = Pe + Ge + Gr – Att – AttBlocking Where: AttBlocking = BlockPR + C/(N+I) + 3 dB
If C/(N+I) = - 3 dB AttBlocking = BlockPR - 3 dB + 3 dB = BlockPR
....equivalent to User Defined Mode
If C/I = 0 dB Broadcast PR Mode...

## Slide 19: Exercise # 4: blocking calculation
Set victim link receiver (VLR)
  Blocking mode: user defined
  Blocking response: function
  Interference criteria: I/N = 0
  Noise level = -110
Set interfering link transmitter (ILT)
  No change
Path between VLR with ILT
  No change

## Slide 20: Victim link

## Slide 21: VLR Blocking Mask
Should be defined at the frequency of the Interferer
Att blocking = 50 dB
(e.g. Defined in ETSI Standards)
fV
fI

## Slide 22: Simulations
IRSS Blocking= Pe + Ge + Gr – Att (free space) – Att block IRSS Blocking= 23 dBm + 0 dB + 0 dB – 111.57 dB – 50 dB IRSS Blocking = - 138.57 dBm

## Slide 23: Results
IRSS Blocking Level = - 138.57 dBm N = -110 dBm I/N = 0 dB (Criterion) always met

## Slide 24: Question?
Can I make simulation for unwanted and blocking in the same workspace?

## Slide 25: Question: Can I make simulation for unwanted and blocking in the same workspace?
2 Interference Criteria / 2 runs

## Slide 26: Question: Can I run simulations for unwanted and blocking in the same workspace in a single run?
If the interference criteria are not the same... You can compensate this when defining the mask (unwanted or blocking)
Blocking: PR mode + Criterion: C/I=0 dB
Unwanted: Criterion C/I=10 dB
Remove 10 dB from blocking mask
Criterion C/I=10 dB

## Slide 27: Questions?
Thanks for your attention