|  | Doc. STG(13)10 |
| --- | --- |
| WGSE STG |  |
| 33rd Meeting of SE STG Copenhagen, Denmark, 6 – 8 February 2013 |  |
| Date issued: | 5 February 2013 |
| Source: | Bundesnetzagentur |
| Subject: | Path loss and propagation models in SEAMCAT |

| Password protection required? (Y/N) |  |
| --- | --- |

# Issue: Underestimation of the path loss for very short distances by the Extended Hata – SRD model

SE24 identified a significant underestimation of the path loss in in the “Extended Hata – SRD” model used in SEAMCAT for very short distances, e.g. below 5 m (see M68 SE24 minutes section 4.6). In this document, this issue is addressed closer and a solution is suggested.

The discussion and tests in PT SE24 have shown that, in special cases, the path loss calculation in SEAMCAT results in negative losses (see Figure 1), this seems not reasonable, because this result would mean  a gain instead of attenuation by the propagation model.

Therefore a propagation test was made with the input parameters presented in Table 1. The result is presented in Figure 1. The result shows that a number of trails are resulting in negativ path loss.

Table 1: Values for Path loss calculation for Figure 1

| Extended Hata - SRD |
| --- |
| Frequency | 900 MHz |
| TX/RX Height | 1.5 m |
| Distance | 0.3m – 1m |
| Environment | Urban |
| Scenario | Indoor - Indoor |
| Variation | Active - default |

Figure 1: Extract of the histogram of path loss (Extended Hata - SRD): below 7.5 dB path loss

The reason for this strange behaviour is that the median or mean path loss is computed correct. However, the added normal distribution with a given standard deviation results in the spreading of the path loss around the median or mean value of the path loss. It has to be highlighted that this result is only producible if the propagation model has a high variation and the distance is low.

Path loss for short distances by the Extended Hata model

The standard deviation is predefined in the extended Hata model. For the case a relative high standard deviation and short distances (e.g. up 200 m) it is likely to occur that the path loss is much lower than free space. The “SEAMCAT implementation of Extended Hata and Extended Hata‐SRD models” available on the SEAMCAT online manual, states - in contradiction to the results - shown in Figure 2 that:

“When L is below the free space attenuation for the same distance, the free space attenuation should be used instead.”

Two examples of the path loss with two models and different standard deviations are given below for illustration.

Table 2: Values for Path loss (Extended Hata) calculation for Figure 2

| Extended Hata |
| --- |
| Frequency | 900 MHz |
| RX Height | 1.5 m |
| TX Height | 30 m |
| Distance | 1m – 200m |
| Environment | Rural |
| Scenario | Outdoor - Outdoor |
| Variation | Active – default: 5.6-12 dB (red curve) |

Table 3:  Values for Path loss (Free Space) calculation for Figure 2

| Free Space |
| --- |
| Frequency | 900 MHz |
| RX Height | 1.5 m |
| TX Height | 30 m |
| Distance | 1m – 200m |
| Variation | Active – sigma = 3.5 (used in Extended Hata in the first 40 m) (blue curve) |

Figure 2: Results of path loss (Extended Hata and Free Space), between 80 to 140 m

In general, the propagation models could be used for very low distances, but the users have to have in mind that the propagation models are fitting best the situation, if the model is used in the far field.

It is obvious that also in the illustrated examples the path loss can be significant underestimated.

Far field – Near field

One important assumption for all propagation models used in SEAMCAT is far field condition for the antennas used: the path length d >> wave length 

The boundary between the far field and near field can be roughly estimated with the assumption of a plane wave front resulting in

2*D2 / 

Where:

d = Distance

= Wavelength

D = maximum dimension of the antenna

Often used is the following far field condition for frequencies in the UHF range or higher.

d ≫  ( d = 11 * 

Or with the assumption of a plane wavefront:

d > 2*D2 / 

With D = results this in:

d > 2*

This distance d should be respected by the use of any propagation model.

## Tree options to address this issue

- Stick to the Free Space path loss if the calculated path loss including the random distribution is less than the free space:

L(d) + T(G(()) ≥ LFree(d)

Advantage: 	Covers both cases described, no path loss < free space

Disadvantage:	Deviates from equation in SEAMCAT manual

Illustration in Figure 3: In this option the blue line is the minimum allowed path loss.

Red curve = L(d) + T(G(())

Blue curve = LFree(d)

Figure 3: Results of path loss (Extended Hata (red) and Free Space (blue)), between 1 to 200 m.

- Stick to the Free Space path loss minus 3 dB if the calculated path loss including the random distribution is less than the free space:

L(d) + T(G(()) ≥ LFree(d) - 3 dB

Advantage:	Allows path loss less than free space, e.g. 2-way propagation

Disadvantage: 	Deviates from equation in SEAMCAT manual

As illustration see Figure 3, note the blue line is then 3 dB lower.

- Stick to the Free Space path loss with a normal distribution of standard deviation 3.5dB as minimum pass loss for the Extended Hata model, in all environments and scenarios. This sigma is used in the first 40m of the model (Free Space part).

L(d) + T(G(()) ≥ LFree(d) + T(G(3.5dB))

Advantage: 	Closer to SEAMCAT manual

Disadvantage:	Path loss could be more than 3 dB below free space which is difficult to explain by the physic (wave guide, resonator??)

Illustration in Figure 4: In this option the blue line is the minimum allowed path loss.

Red curve = L(d) + T(G(())

Blue curve = LFree(d) + T(G(3.5dB)

Figure 4: Results of path loss (Extended Hata (red) and Free Space (blue)), between 1 to 200 m.

# Text boxes

N