## Slide 1: Future Spectrum for RFID, Smart Metering and SRDs in the UHF Frequencies WGFM Civil/Military Meeting Dublin, 26-27 November 2013 Thomas Weber (ECO), SRD/MG Chairman

## Slide 2: Content
Demand expressed
Situation 863-870 MHz
Significant Considerations
Existing usage 870-876/915-921 MHz
Investigations in the ECC and Results
Foreseen Band Plans
The “SRD” Approach

## Slide 3: Demand Expressed
  ETSI published 5 System Reference Documents:
  Generic SRD, RFID, Home Automation & Sub Metering and Automotive SRD, TR 102-649-2;
  Smart Meters and Smart Grids, TR 102 886;
  Metropolitan Mesh Machine Networks (M3N) applications, TR 103 055;
  Alarm and Social Alarm systems, TR 103 056 and
  Assistive Listening Devices, TR 102 791.
  These devices have a huge significance in our daily lives, whether as assistance for people with a hearing impairment, or bringing down the costs of supermarket goods, or as part of making an intruder alarm system affordable, to give just three examples.

## Slide 4: 863-870 MHz (Existing SRD Range) Survey – End of 2010
  At present the range 863 to 870 MHz is used extensively for SRD applications. However, these ranges are filling up quickly and a lot of new developments are anticipated, as by ECC Report 182 (Survey about the use of the frequency band 863-870 MHz)
24 responses representing > 1 million devices (e.g. one responder stating that it was rather 10 millions instead of 1 million devices);
14 responses representing > 100 000 devices;
25 responses representing less than 100 000 devices (but more than 1 000):
10 responses representing less than 1 000 devices (but more than 100);
1 response indicating less than 100 devices.
-> per annum; in 863-870 MHz, device population increase
-> only those who responded (real numbers must be higher)

## Slide 5: Significant Considerations
  Not only capacity constraints, the bandwidth of the existing plans is limiting to developing applications, e.g. improve their performance and function.
  On the American continent nearby frequencies (902 to 928 MHz) are allocated to ISM, which is a convenient basis for using SRDs, and therefore a lot of equipment is being developed to operate in this range.
  For Europe, as part of the ITU-R Region 1, no ISM band was identified at the World Administrative Radiocommunication Conference (WARC-79 ) in 1979 in this part of the spectrum.
  Frequencies which are seriously under-utilised in many countries: namely 870 - 876 MHz, and 915 - 921 MHz; these are frequencies which had been prepared for use by private mobile radio systems, but that development has seen very little take-up.

## Slide 6: Existing usage 870-876/915-921 MHz
Chart: Existing Usage, also taking into account current planning (43 of countries)
| No usage- whole bands | No usage - part of bands | PMR/PAMR | military/governmental | Planned future E-GSM-R
Usage Level 862-863 based on x Answers | 22 | 12 | 4 | 11 | 5

## Slide 7: Investigations in the ECC and Results
  ECC Report 200 gives the background and conclusions to a comprehensive set of coexistence studies in these under-utilised UHF bands in Europe.
  The related ECC Report 189 uses these conclusions to define recommended regulatory parameters for SRDs. It is expected to form part of the ECC’s key regulatory document on SRDs, Recommendation 70-03.
  Although under-utilised for Professional Mobile Radio (PMR), there are significant existing governmental services with access to part of these frequencies in several countries which would need protection in the future at the discretion of the relevant national administrations. The review included an audit of these existing and planned uses, which revealed not only some of the military tactical systems as known about, but also some new uses such as remote control of unmanned aircraft (UAV).
  Some other countries anticipate needing to use the spectrum in some specific locations for an extension of the existing GSM-R bands. The studies in the ECC have covered this utilisation to provide a solution for spectrum sharing with GSM-R.

## Slide 8: Band Plan 870-876 MHz and Related Use of Mitigation Techniques
Duty Cycle Mitigation is very dominant !

## Slide 9: Band Plan 915-921 MHz
Note:
RFID/ALD sharing
Safe harbours
Symmetry
Flat SRD regulation
RFID DAA for E-GSM-R

## Slide 10: SRD Approach
  No ECC Decision!
  This particular approach provides a good example of the ECC's use of ‘soft harmonisation’, where existing services remain protected to the extent that national administrations deem it necessary, yet providing the opportunity for the harmonised development of new services in the majority of European countries.
  The success of ERC Recommendation 70-03 owes much to its ‘soft harmonisation’ approach, which is quicker to set up than a more rigid, centralised harmonisation process, where the measures needed to deal with important but limited incumbent interest can block or delay the process at the European level.
  Administrations can freely decide which part of the ERC/REC 70-03 new entries they can implement – in line and in balance with incumbent use.

## Slide 11: Thank you for your attention
Thomas.Weber@eco.cept.org
www.cept.org/eco
www.cept.org/ecc
Questions??