SEAMCAT IMPLEmentation of winner and itu propagation models

references	1

1.	WINNER Propagation models	2

2.	ITU P 452 model	3

2.1	Line-of-sight propagation (including short-term effects) source ITU P452	3

2.2	Clutter loss calculation: source height-gain model (ITU – R P452 page 15)	4

2.3	Sub path diffraction model source: ITU P526 page 13	5

3.	ITU Winner path loss models – Results comparison	5

3.1	Scenario WINNER C1	6

3.2	Scenario WINNER C2	6

3.3	Scenario WINNER D1	6

4.	ITU P452model – Results comparison	7

4.1	Scenario 1	7

4.2	Scenario 2	7

4.3	Scenario 3	8

# references

Recommendation ITU –R P 452-12

ERC REPORT 68 Monte Carlo simulation methodology for the use in sharing and compatibility studies between different radio services or systems, Naples, February 2000, revised in Regensburg, May 2001

Recommendation ITU - R P 526-9

Annex 10, Determination of the basic transmission loss in the Fixed Service

# WINNER Propagation models

Source WINNER Phase I Deliverable D5.4 v1.4 (page 26)

Path-loss models at 5 GHz for considered scenarios have been developed based on measurement results or from literature. The developed path models are presented in Table 1 including the shadow fading values.

Table 1: Path-loss models

| Scenario | Path loss [dB] | Shadow fading standard dev. | Applicability range |
| --- | --- | --- | --- |
| C1 | LOS | 23.8 log10 (d) + 41.6 40.0 log10 (d/dBP) + 41.6 + 23.8 log10(dBP) ****) +) | σ = 4.0 dB σ = 6.0 dB, | 30 m < d < dBP dBP < d < 5 km |
|  | NLOS | 40.2 log10 (d[m]) + 27.7 **) | ( = 8 dB | 50 m < d < 5 km |
| C2 | NLOS | 35.0 log10 (d[m]) +38.4 ***) | ( = 8 dB | 50 m < d < 5 km |
| D1 | LOS | 21.5 log10 (d[m]) + 44.6 40.0 log10 (d/dBP) + 44.6 + 21.5 log10 (dBP) ****) +) | ( = 3.5dB ( = 6.0dB | 30 m < d < dBP dBP < d < 10 km |
|  | NLOS | 25.1 log10 (d[m]) + 55.8 | ( = 8.0dB | 30 m < d < 10 km |

**) Validity beyond 1 km not confirmed by measurement data.

***)  Validity beyond 2 kms not confirmed by measurement data.

****)  dBP is the break-point distance: dBP = 4 hBS hMS / λ, where hBS is antenna height at BS, hMS is antenna height at MS, and λ is the wavelength. Validity beyond dBP not confirmed by measurement data.

+)  BS antenna heights in the measurements: C1 LOS: 11.7 m, D1: 19 – 25 m.

Note C1 – SUBURBAN, C2 – URBAN, D1 – RURAL

# ITU P 452 model

This includes the implementation of equation 8(b). This is the summation of line of sight model, addition losses due to clutter loss models and sub path diffraction models.

Table 2: Methods of deriving overall predictions

| Path type | Model description |
| --- | --- |
| Line-of-sight | The prediction is obtained by summing the losses given by the line-of-sight and clutter loss models, i.e.: Lb ( p) = Lb0 ( p) + Aht + Ahr dB (8a) where: Lb0 ( p) : predicted basic transmission loss not exceeded for p% of time given by the line-of-sight model Aht, Ahr : appropriate additional losses due to height-gain effects in local clutter |
| Line-of-sight with sub-path diffraction | The prediction is obtained by summing the losses given by the line-of-sight and (sub-path) diffraction models and clutter models, i.e.: Lb ( p) = Lb0 ( p) + Lds ( p) + Aht + Ahr dB (8b) where: Lds ( p): prediction for p% of time given by the sub-path diffraction loss element of the diffraction model |

## Line-of-sight propagation (including short-term effects) source ITU P452

The basic transmission loss Lb0 ( p) not exceeded for time percentage, p%, due to line-of-sight propagation is given by:

Lb0 ( p) = 92.5 + 20 log f + 20 log d + Es ( p) + Ag                dB

where:

Es ( p) :	correction for multipath and focusing effects:

Es ( p) = 2.6 (1 – e– d / 10) log ( p / 50)                dB

Ag :	total gaseous absorption (dB):

Where: γo, γw(ρ) :	specific attenuation due to dry air and water vapour, respectively and ρ is water vapour density.

Calculation of attenuation due to atmosphere: source ERC Report 68 page 22

Note: the water vapour density ( is a variable. In the model set to 3 g/m3 (ERC Report 68 page 22)

## Clutter loss calculation: source height-gain model (ITU – R P452 page 15)

The additional loss due to protection from local clutter is given by the expression:

where:

dk :	distance (km) from nominal clutter point to the antenna (see Fig. 3)

h :	antenna height (m) above local ground level

ha :	nominal clutter height (m) above local ground level.

Table 3 - Nominal clutter heights and distances

| Clutter (ground-cover) category | Nominal height, ha (m) | Nominal distance, dk (km) |
| --- | --- | --- |
| Category 1 High crop fields Park land Irregularly spaced sparse trees Orchard (regularly spaced) Sparse houses | 4 | 0.1 |
| Category 2 Village centre | 5 | 0.07 |
| Category 3 Deciduous trees (irregularly spaced) Deciduous trees (regularly spaced) Mixed tree forest | 15 | 0.05 |
| Category 4 Coniferous trees (irregularly spaced) Coniferous trees (regularly spaced) | 20 | 0.05 |
| Category 5 Suburban | 9 | 0.025 |
| Category 6 Dense suburban | 12 | 0.02 |
| Category 7 Urban | 20 | 0.02 |
| Category 8 Dense urban | 25 | 0.02 |
| Category 9 Industrial zone | 20 | 0.05 |

Note: in the clutter loss model the clutter category is a variable that needs to be initialised according to the scenario. In the model set to clutter category 2

## Sub path diffraction model source: ITU P526 page 13

The diffraction loss (A) in terms of the first Fresnel zone radius, R1 is given as the following.

Where h is path clearance and Ah is the diffraction loss at the horizon

The diffraction loss at the horizon (Ah) is calculated using diffraction field length formulae given in section 3.1.1.2 (page 7) of ITU – R P526. In this case (diffraction loss at horizon) the path length d (km) is given as

where h1 and h2 are transmitter and receiver heights, ae is the  effective radius of the Earth, ae is considered as 8500km (ERC report 68, page 23), h1, h2, h  and d are in self consistent units.

When calculating Ah the value of ( = 1 (this parameter allows for the type of ground and polarization, ITU P526 page 7), the value of K = 10-5 (Normalized earth surface admittance factor, ERC report 68 page 23)

# ITU Winner path loss models – Results comparison

The following results comparisons are made between SC Java Plug-in Modules and the Matlab Implementation

Source Document: Winner Phase I Deliverable D5.4 Version 1.4 – page 26

Selected models: C1 (LOS and NLOS), C2 (LOS and NLOS), D1

C1 LOS – distances between 30m to 5km

C1 NLOS – distances between 50m to 5km

C2 – distances between 50m to 5km

D1 – distances between 30m to 10km

Breakpoint distance is assumed as 1000m in the case of following test results

## Scenario WINNER C1

| Matlab Implementation | Seam Cat Java Plug-in Module |
| --- | --- |

## Scenario WINNER C2

| Matlab Implementation | Seam Cat Java Plug-in Module |
| --- | --- |

## Scenario WINNER D1

| Matlab Implementation | Seam Cat Java Plug-in Module |
| --- | --- |

# ITU P452model

## Results comparison

The following results comparisons are made between SC Java Plug-in Modules and the Matlab Implementation

### Scenario 1

Clutter category = 1 (ha = 4m, dk = 0.1 km)

Tx height = 10m

Rx height = 1.5m

| Matlab Implementation | Seam Cat Java Plug-in Module |
| --- | --- |

### Scenario 2

Clutter category = 1 (ha = 4m, dk = 0.1 km)

Tx height = 10m

Rx height = 1.5m

P = 50%

| Matlab Implementation | Seam Cat Java Plug-in Module |
| --- | --- |

### Scenario 3

Clutter category = 1 (ha = 4m , dk = 0.1 km)

Tx height = 10m

Rx height = 1.5m

P = 20%

| Matlab Implementation | Seam Cat Java Plug-in Module |
| --- | --- |

## Comparison between P452-12plug-in module implemented in SEAMCAT and ITU-R P.452-12 excel model

### ITU-R P.452-12 loss

FIGURE 1: Path loss attenuation with respect to percentage time

Calculations are based on a flat terrain model with sub path and without any clutter

Tx height = 10m

Rx height = 1.5m

P = 20%

### Conclusion

When comparing ITU-R P.452-12 model and the plug in module based on the same set of input parameters of Tx /Rx, frequency, and considering sub path without clutter, it can be observed some dB difference in the loss results.