## Slide 1: Session 3 Major topics on spectrum – WG FM
Presented by Robin Donoghue

## Slide 2: Contents
Private 5G Networks
Railway Communications GSM-R to FRMCS
Satellite
Automotive
Drones
Wireless Charging
Jammers

## Slide 3: Private 5G networks
FM60 was set up to Develop a harmonised frequency arrangement and harmonised technical conditions for the shared use of the 3.8-4.2 GHz.
CEPT Report 088 and ECC Decision (24)01 published in November 2024.
FM60 now developing a new ECC Recommendation to provide national guidance on the shared use of the 3.8-4.2 GHz band for WBB LMP
Notes: Note the Paris opening ceremony. Note the TV2 studio in Tivoli. Driverless trucks in Sweden.
The commission would like to Harmonise the use – so mandated CEPT to provide guidance – the CEPT Report. Wireless Broad-Band Low and Medium Power. Differing National and Industry views on what Shared Use means.

## Slide 4: Railway Communications GSM-R to FRMCS
Currently Rail communication works on a 2G system called GSM-R.
FM56 was set up to work on spectrum issues related to railway applications, especially GSM-R and its successor.
In 2017 ETSI published the System Reference document (SRDoc) TR 103 333 requesting FRMCS.
ECC Decision (20)02 was published in June 2020. The EU has now mandated CEPT to suggest harmonised technical conditions. Draft CEPT Report 90.
Notes: Rail safety systems need to be proven technologies – 2G systems still being deployed. Prime UHF spectrum – Goldilocks Zone.
Global System for Mobile Communication for Rail being replaced by Future Rail Mobile Communications System. Draft CEPT Report 90 is currently in Public Consultation.

## Slide 5: Satellite
Galileo is an EU funded independent high-precision GNSS system with greater accuracy than GPS. However, it shares 1258-1300 MHz spectrum with Amateur Radio. Draft ECC Decision (25)01, setting out the shared use is currently under public consultation.
FM44 developed an ECC Report on the regulatory analyses of satellite use in the band 862-870 MHz to communicate with terrestrial SRD. Draft ECC Decision (25)02 is currently under public consultation.
Notes: 1980s Ronald Reagan first allowed the commercial use of GPS GNSS (Sat Navs). Initially Degraded capability compared to military. Bill Clinton allowed improved precision. Use is not just navigation. The timing signals are essential for banking and trading.
Galileo intended to give better user experience. Funded through ESA. Amateurs have complained that one element of Galileo is co-channel with their Secondary use.
IoT and remote sensors need to communicate. Mainly Uplink reporting. Satellite is the ideal receiver. Uses SRD type technical parameters. Low power, low duty cycle. Highly directional antenna assumed for satellite communications. But for very low data rates, some new Mobile Handsets (iPhone 16) have shown this can work.

## Slide 6: Automotive
Intelligent Transport Systems (ITS)
  ITS was originally allocated 5875-5925 MHz in 2008 on a request for a very specific list of automotive applications and it envisioned the extensive roll-out of road infrastructure as well as enabled vehicles.
  Two technology visions, ETSI G5 and LTE-V
  ECC Decision (08)01 recently changed to allow 20 MHz channels
  24 January 2025 the EU Mandated to CEPT on ITS wider channels.
Notes: ITS initially envisioned in 2006 as the step towards driverless vehicles. However, this would need infrastructure at every junction and hazard. Highly promoted by the auto industry. Less so by tax-payers. To date infrastructure mainly on trunk roads, not the last mile.
Meanwhile, a second technology was developed. Difficult to share spectrum between a polite and a sequenced technology.

## Slide 7: Automotive
Short Range Radar (SRR)
  SRR are now commonplace on many new vehicles
  They are the sensor behind automated braking, adaptive cruise control and is some cases parking assist.
  Long range (pencil beam) and Short Range (UWB)
  Operating around 80 GHz – potential impact on other spectrum users such as Radio-Astronomy
  Ongoing studies – usually in SE24.
Notes: Initially at 24 GHz. Long term home is 79 GHz.

## Slide 8: Drones
ECC Recommendation (24)02 guidance on governmental UAS (Drones) 1880-1900 MHz and 1910-1920 MHz
Control of the Drone
Spectrum for Payload
Autonomous or controlled (or both!)
ERC Recommendation 70-03 Annex 3 for WBDTS using FHSS at 100mW but low range line of sight to the controller.
Notes: Uncrewed Arial Systems (UAS), WIDEBAND DATA TRANSMISSION SYSTEMS, Frequency Hopping Spread Spectrum.
Hobby and Toy drones work on 2.4 GHz using technology originally developed by the WiFi industry (FHSS). However, these must remain in Line of Sight. E.g. in the UK CAP722.
Likely technology for 1900 MHz drones is DECT-NR.

## Slide 9: Wireless charging
WPT
  New ECC Recommendation (25)01. Has for first time set the correct regulatory framework for WPT.
  Previously placed on the market as either SRD or non radio devices under the ECM Directive.
  Now higher power and additional frequency bands being considered,
WPT-EV Electric vehicle charging
  How to charge a 60 kWh battery?
  Ongoing studies.
Notes: Rec (25)01 is intended to be expanded – just like rec 70-03 for SRDs.
Electric Vehicles – consumer looking for convenience and safe charging. Very low frequencies used for military communications (submarines) standard frequency and time and LF broadcasting.

## Slide 10: Jammers
Jammers are illegal
  No lawful way to place a Jammer on the European Single Market under the Radio Equipment Directive (RED)
  No lawful use (unless you are the National Security services)
  ECC Recommendation (04)01 recently amended to make more explicit the rules and also to discourage the ownership of Jammers.
Notes: RED – New Approach Directive. Replaced the RTTE in 2014. Previous tom 1999, Golden Standard equipment. Now every single product needs to be compliant.

## Slide 11: Contact
Robin Donoghue
Spectrum Management
ECO
Nyropsgade 37, 4 1602 Copenhagen Denmark T: +45 31 32 76 71 F: +45 33 89 63 30
robin.donoghue@eco.cept.org