## Slide 1
Session 3 Major topics under consideration in ECC – Spectrum issues
Presented by Doriana Guiducci
CEPT workshop on Spectrum, Numbering, ITU Policy, and Postal Regulation
European Communications Office, 20-21 March 2025

## Slide 2: What´s up on the mobile service
5G & 6G
  CEPT Roadmap
6 GHz band
  Lower and Upper
Preparation to WRC-27
  IMT
  Direct to device

## Slide 3: Where to start
The ITU´s 2023 World Radiocommunication Conference (WRC-23) agreed a range of new allocations and technical conditions to enable 5G and 6G and ensure protection of existing users
6425-7125 MHz identified for IMT to enable 5G and future 6G The use of the band for RLAN is recognised
Mobile bands below 3 GHz for “high altitude platforms operating as IMT base stations” (HIBS)
470-960 MHz (UHF band) reviewed, with a new secondary mobile allocation created in 470-694 MHz encompassing most CEPT countries. This allows countries to deploy mobile networks while ensuring TV broadcasting can continue to use the band. Possible further actions in the wider UHF at WRC-31
Upgrade of allocation in 3.6-3.8 GHz.
Additional IMT identifications in some countries and regions outside Europe in 3.3-3.4 GHz, 3.6-3.8 GHz and 10-10.5 GHz
WRC-23 20 November-15 December 2023 Dubai – UAE
source: ITU

## Slide 4: What´s ´6G´?
6 usage scenario for IMT-2030
  eMBB  Immersive Communication
  mMTC  Massive Communication
  uRLLC  HRLLC (Hyper Reliable & Low Latency Communication)
  Ubiquitous Communication
  AI and Communication
  Integrated Sensing and Communication
4 overarching aspects that act as design principles commonly applicable to all usage scenarios:
  Sustainability
  Connecting the unconnected
  Ubiquitous intelligence
  Security/resilience
The “Wheel diagram”, Recommendation ITU-R M.2160
Source: ITU-R Recommendation M.2083

## Slide 5: IMT-2030 Capabilities
The Framework Recommendation identifies 15 capabilities for IMT-2030
  9 of those capabilities are derived from existing IMT-2020 systems
The range of values given for capabilities are estimated targets for research and investigation of IMT-2030
  All values in the range have equal priority in research and investigation
IMT-2030 is expected to help address the need for increased environmental, social and economic sustainability and also support the goals of the Paris Agreement of the United Nations Framework Convention on Climate Change
The “Palette diagram”, Recommendation ITU-R M.2160

## Slide 6: ECC activites – the CEPT roadmap for 6G
The CEPT roadmap for 6G has been approved in November 2024
The roadmap highlights the main strategic phases of 6G from research to commercial launch.
5 main tasks are identified with the related actions and activities in ECC:
  Harmonisation
  WRC-23 follow up
  WRC-27
  Other spectrum challenges
  Numbering aspects
  The work is still in its early stage. The roadmap is a live document that will be amended while the work on 6G progresses

## Slide 7: Evolution of WAS/RLAN
The most recent evolutions of the IEEE 802.11 standard (Wi-Fi6E & Wi-Fi7) include the use of the 6 GHz band with channels up to 320 MHz
The lower 6 GHz is already harmonised in Europe
source: Wi-Fi Alliance

## Slide 8: Harmonisation of the ´Lower 6 GHz´ band
2017
2024
2018
2019
2020
2021
2022
2023
Lower 6 GHz 5945−6425 MHz
Coexistence studies with WAS/RLANs
ECC DEC (20)01
ECC Rep 355
Out-of-band VLP emission limits
Review of ECC DEC (20)01
Updated ECC DEC(20)01
Harmonisation of the band for LPI and VLP
Higher power
2027
ECC Rep 302
ECC Rep 316
Short-term protecion of fixed service
2025
2026
VLP Mitigation
SE45
FM57FM61
Forum Group
CEPT REP 75
CEPT REP 87
  LPI: Low power indoor device
  VLP: Very low power device

## Slide 9: Harmonisation of the ´Upper 6 GHz´ band
2024
2023
Coexistence of WAS/RLANs with existing services
ECC Rep 364
MFCN and WAS/RLAN sharing
IMT identification RLAN use recognised
2027
2025
2026
PT1
EC Mandate
Draft ECC Rep 366
2022
SE45
MFCN vs incumbents
Mandate Task 1
WBB ECS & RLAN vs incumbents
Mandate Task 2
WBB ECS & RLAN shared use
Mandate Task 3
Harmonisation
PT1 - WGFM
  These are to be intended as synonyms:
  IMT: International Mobile Telecommunications
  MFCN: Mobile/Fixed communications networks
  WBB ECS: Wireless Broadband Electronic Communications Services
Upper 6 GHz 6425-7125 MHz

## Slide 10: ECC – harmonisation of the 6 GHz band
Technical studies in ECC:
  Sharing and compatibility studies related to Wireless Access Systems including Radio Local Area Networks (WAS/RLAN) in the frequency band 6425-7125 MHz – ECC Report 364
  Study and assessment of coexistence and compatibility of MFCN in upper 6 GHz band with incumbent spectrum users
  Feasibility and sharing studies on the potential shared use of the 6425-7125 MHz frequency band between Mobile/Fixed Communication Networks and WAS/RLAN – draft ECC Report 366 (under public consultation)
EC Mandate to CEPT on the potential shared use of the 6425-7125 MHz band:
  Task 1 on the coexistence of Wireless Broadband Electronic Communications Systems (WBB ECS) and WAS/RLAN versus incumbents
  Task 2 on the potential shared use between WBB ECS and WAS/RLAN
  Task 3 on the harmonised technical conditions

## Slide 11: Spectrum for mobile: what´s next?
WRC-23
WRC-27
Possible new IMT identifications for 5G and 6G in the bands (or parts thereof):
  4400-4800 MHz in Region 1 (EMEA) and 3 (Asia)
  7125-7250 and 7750-8400 MHz in Region 1;
  7125-8400 MHz in Region 2 (Americas) and 3;
  14.8-15.35 GHz globally
4 YEARS OF
GLOBAL PREPARATION
6425-7125 MHz identified for IMT to enable 5G and future 6G The use of the band for RLAN is recognised
Mobile bands below 3 GHz for “high altitude platforms operating as IMT base stations” (HIBS)
470-960 MHz (UHF band) reviewed, with a new secondary mobile allocation created in 470-694 MHz encompassing most CEPT countries. Possible further actions in the wider UHF at WRC-31
Upgrade of allocation in 3.6-3.8 GHz.
Additional IMT identifications in some countries and regions outside Europe in 3.3-3.4 GHz, 3.6-3.8 GHz and 10-10.5 GHz
source: ITU

## Slide 12: IMT 4.4, 7, 8 & 15 GHz - European Common Allocations (1/2)
4400 – 4800 MHz
14.8 – 15.35 GHz
The European Table of Frequency Allocations and Applications (ECA Table) provides the main usage of spectrum within CEPT countries for the frequency range from 8.3 kHz to 3000 GHz https://efis.cept.org/sitecontent.jsp?sitecontent=ecatable

## Slide 13: IMT 4.4, 7, 8 & 15 GHz - European Common Allocations (2/2)
7125-7250 MHz ….
14.8 – 15.35 GHz
…. and 7750-8400 MHz

## Slide 14: Direct to Device/Cell Connectivity
Satellite connectivity ready to be provided in the bands already allocated to the Mobile-Satellite Service
3GPP has specified NTN bands in Release 17:
  n255 (1626.5-1660.5 (Earth-to-space) / 1525-1559 MHz (space-to-Earth)
  n256 (1980-2010 (Earth-to-space) / 2170-2200 MHz (space-to-Earth)
  Others under study for Release 18 and beyond
WRC-27 will discuss possible new allocations to MSS in the frequency bands:
  2010-2025 MHz (Earth-to-space) and 2160-2170 MHz (space-to-Earth) in Regions 1 and 3
  2120-2160 MHz (space-to-Earth) in all Regions
In bands allocated to the mobile-satellite service MSS
In bands allocated to the mobile service MS
Direct connectivity between space stations and IMT user equipment is not currently internationally recognised/protected in bands allocated to MS
WRC-27 will discuss possible new allocations to MSS in 694/698 MHz and 2.7 GHz, taking into account Recommendation ITU-R M.1036
Challenges:
  Interference issues
  Cross-border issues
  Specific Regional/National circumstances

## Slide 15: To know more
Spectrum for wireless broadband:
  5G/5G&beyond
  Towards 6G communications
ECC Newsletter
  WRC_23 outcomes
  What´s on the WRC-27 agenda
ASK! 
Doriana.Guiducci@eco.cept.org