## Slide 1: ECC Roadmap for 5G Spectrum below 3.4 GHz The European 5G Conference 2018
Eric Fournier
Chairman, Electronic Communications Committee

## Slide 2: CEPT 5G Roadmap
    CEPT 5G Roadmap
    https://cept.org/ecc/topics/spectrum-for-wireless-broadband-5g
    Besides harmonisation for 3.4-3.8 GHz and 26 GHz, the objective is to review ECC decisions in MFCN bands to ensure they are suitable for 5G:
    Further considerations expected from ECC/PT1 for 700MHz, 800MHz, 900MHz, 1800MHz, 2.1GHz, 2.3GHz, 2.6GHz
    Note the outcome of harmonisation work for the L band

## Slide 3: Does 5G arrive in lower bands?
Yes, 5G NR will be specified in Release 15 bands in all CEPT bands with FDD plans
In addition, 5G NR will be specified in the 1.5 GHz (SDL) and 2.6 GHz unpaired band (TDD)
… and carrier aggregation will enable combining lower bands with 3.4-3.8 GHz
INDUSTRY WANTS 5G IN LOWER BANDS NOW
Below 1 GHz | Above 1 GHz
700 MHz | 1.8 GHz
800 MHz | 2.1 GHz
900 MHz | 2.6 GHz

## Slide 4: What is needed?
5G NR remains compatible with existing frequency arrangements and block size multiple of 5 MHz
Active Antenna Systems (AAS) impact how to define Block Edge Mask (BEM) : TRP vs EIRP above 1 GHz ?
900/1800 MHz are not technology neutral (GSM bands)
        900/1800 MHz with BEM ?
        900 MHz range quite “busy”: GSM-R, FRMCS, SRD …
        Is it possible to simply translate BEM into TRP? Guard bands in 2.1 GHz not affected ?
        Are 700/800 MHz “5G ready”?
Next ECC meeting to address timeline and priorities