## Slide 1: The Upper 6GHz band (6425-7125 MHz): Where we are in CEPT
16th European Spectrum Management Conference
23-25 June 2021
Tuck Yeen Poon, CEPT Coordinator for WRC-23 AI 1.2 ,
Ofcom, United Kingdom

## Slide 2: Agenda Item 1.2: Upper 6 GHz
Frequency Bands - Agenda Item 1.2
Agenda Item 1.2 will be discussed in ECC PT1 (CEPT) and WP 5D (ITU-R).
Resolution 245 considers IMT identification in Region 1 for the entire 6 425 – 7 125 MHz frequency band, while global identification is only considered for 7 025 – 7 125 MHz frequency band.
Dateline to finalise the technical and operational characteristics from relevant ITU-R groups is 23rd July 2021.
Sharing and compatibility studies to be conducted on primary service (*and in adjacent band, as appropriate).
There are interest from a wide range of stakeholders (next slide).
3 300
MHz
3 400
MHz
3 600
MHz
3 800
MHz
6 425
MHz
7 025
MHz
7 125
MHz
10
GHz
10.5
GHz

## Slide 3: Sharing and Compatibility Study
5 925 MHz
7 075 MHz
7 145 MHz
6 700 MHz
Primary Allocations in Radio Regulation
Other services
Earth exploration-satellite (passive) (6 425 – 7 075 MHz and 7 075 – 7 250 MHz) - RR 5.458
Radio astronomy (6 650 – 6 675.2 MHz) - RR 5.149
Space Operation Service (additional primary allocation for Russian Federation in 7 100 – 7 155 MHz) - RR 5.459
6 425 MHz
Upper 6 GHz under AI 1.2
FIXED 5.457
FIXED SATELLITE (E-s) 5.457A 5.457B
MOBILE 5.457C
5.149 5.440 5.458
FIXED
FIXED SATELLITE (E-s) (s-E) 5.441
MOBILE
5.458 5.458A 5.458B
FIXED
MOBILE
5.458 5.459
7 125 MHz

## Slide 4: Initial CEPT AI 1.2 discussions
5 925 MHz
7 075 MHz
7 145 MHz
6 700 MHz
FIXED
FIXED SATELLITE (E-s)
MOBILE
Earth Exploration-Satellite (passive)
5.149 5.440 5.458
FIXED
FIXED SATELLITE (E-s) (s-E) 5.441
Earth Exploration-Satellite (passive)
5.458 5.458A 5.458B
FIXED
Earth Exploration-Satellite (passive)
5.458
European Common Allocation (ECA) Table
Upper 6 GHz under AI 1.2
6 425 MHz
7 125 MHz
Notes
There are some interest for Fixed Satellite usage in the 7 075 – 7 125 MHz
There are interest for Radio astronomy usage in 6 650 – 6 675.2 MHz – RR 5.149
There are interest for Space Operation and Space Research in 7 100 – 7 250 MHz

## Slide 5: Where we are on the upper 6 GHz in CEPT
Still at a very early stage in deciding CEPT’s approach to the upper 6 GHz.
Studies need to be conducted to understand the coexistence situation.
The necessary conditions need to be in place if IMT is to be considered in the band.
There is good cooperative spirit within the CEPT AI 1.2 discussions.

## Slide 6
ECC Contact | Web www.cept.org/ecc
ECO Nyropsgade 37, 4th floor DK-1602 Copenhagen Tel:+45 33 89 63 00 E eco@eco.cept.org |