## Slide 1: Radio spectrum for future railway applications
Thomas Weilacher
Chairman CEPT/ECC Working Group Frequency Management (WG FM)
WWRF, 31 October 2018, Herning / Denmark

## Slide 2: RMR
GSM-R
LTE?
NR?
Beyond
FRMCS project
RMR = Railway Mobile Radio
umbrella term for GSM-R, FRMCS…

## Slide 3: Radio spectrum for the present of RMR
Today 876 - 880 MHz / 921 -925 MHz harmonised for GSM-R
    2x4 MHz for GSM-R only
    Commission Decision 1999/569/EC
    ECC/DEC/(02)05
    Difficult coexistence with MFCN above 925 MHz  see ECC Report 229 and GSM-R improved cab-radios as per TS 102 933-1 v1.3.1 onwards
No spectrum harmonisation of 873 - 876 MHz / 918 - 921 MHz
    Only on a national basis
    3 countries so far: Germany, Switzerland and Liechtenstein (rights of use) + planned in Belgium

## Slide 4: Commission Implementing Decision (EU) 2018/1538 on SRD in 874 - 876 MHz / 915 - 921 MHz
Published on 11 October 2018
2 x 1.6 MHz preserved for railways !
Article 3(4)
    Member States shall refrain from introducing new uses in the 874.4 - 876 MHz and 919.4 - 921 MHz sub-bands until such time as harmonised conditions for their use are possibly adopted under Decision No 676/2002/EC.

## Slide 5: Commission Implementing Decision (EU) 2018/1538 on SRD in 874 - 876 MHz / 915 - 921 MHz
Potential sharing with Defence

## Slide 6: Radio spectrum for the future of RMR
Mandate from the European Commission
CEPT tasks
    FRMCS spectrum needs (only for critical applications)
    Feasibility of the 900 MHz range while ensuring parallel operation with GSM-R during the migration
    Feasibility of the 1900-1920 MHz band (and further bands if relevant)
    Feasibility to use commercial mobile networks
    Develop harmonised technical conditions
Target date: November 2020 for the response

## Slide 7: Organisation of work at ECC
PT1: LRTC derivation for RMR (MFCN as victim)
SE7: RMR as victim
from MFCN and SRD
Bands investigated for harmonisation:
    874.4 - 880 MHz / 919.4 - 925 MHz FDD
    10 MHz in the lower part of 1900 - 1920 MHz TDD
    10 MHz in 2290 - 2400 MHz TDD as a tuning range
FM56: RMR regulation / harmonisation

## Slide 8: LRTC for RMR based on coexistence with MFCN
RMR BS getting closer to MFCN BS UL band within band #8 duplex gap
duplex gap
in-band blocking
RMR TDD
MFCN TDD
RMR BS adjacent to MFCN BS UL band
Potential synchronisation issue between RMR and MFCN when adjacent
2290-2400 MHz tuning range
Telemetry and video PMSE are common in the band: see ECC Report 172

## Slide 9: Key coexistence studies at 900 MHz
RMR DL
RFID
RFID & SRD in data networks
RFID & SRD in data networks
918,7 MHz
917,5 MHz
916,3 MHz
921
918
925 MHz
Non-specific SRD
919,4
917,4
802.11ah
876
874
880 MHz
874,4
SRD in data networks
RMR UL
Band #8 UL
Band #8 DL
Similarly to ETSI TS 102 933-1 v1.3.1 onwards on improved GSM-R radios, it is expected that FRMCS radios will need improved receiver characteristics compared to those currently defined by 3GPP for band #8/n8, in order to ensure a sustainable coexistence with MFCN emissions above 925 MHz and SRD emissions below 919.4 MHz.
impact on cab-radios and EDOR
impact on BS

## Slide 10: Possible scenario: making use of GSM-R white spaces
Benefits:
Offering greater capacity than an LTE 1.4 MHz channel
Having more frequency space for a receiving filter on the cab-radio at each edge of the channel
A 5 MHz carrier in 920-925 MHz would have lower power restrictions than a 1.4 MHz carrier in 919.6-921 MHz
Flexible migration from GSM-R to FRMCS
Why NR and not LTE ?
To avoid LTE’s 6 central RBs mandatory for synchronisation and broadcast information
To benefit from NR’s flexible scheduling (time/frequency and user specific) for system information
Principles: use 5G NR and…
switch off RBs overlapping existing GSM-R carriers
use the remaining available RBs to schedule FRMCS traffic
In this example at HO point, f1 to f4 would require switching off 10 RBs, leaving 15 RBs usable for FRMCS traffic
Figure: Kapsch CarrierCom

## Slide 11: To FRMCS and beyond! A possible ending
Core band: 874.4 - 880 MHz / 919.4 - 925 MHz FDD
    Both GSM-R and FRMCS, including guard-band towards SRD
Complementary band: probably 1900 - 1910 MHz TDD
    Or 10 MHz in 2290-2400 MHz TDD as a tuning range
    FRMCS only

## Slide 12: Some key questions (not exhaustive)
What outage criterion for critical railway usage?
    What criterion? e.g. C/(N+I), INR or minimum bit rate?
    Which threshold?
    Which probability?
What NR numerology for railways?
    Location/speed dependent?  Railway stations, shunting yards, conventional lines, high-speed lines, etc.
    Application dependent? (within critical applications)
Can railways benefit from beamforming?
How to avoid/minimise transmission of critical video stream?
    On-board processing, specific codec, etc. based on railway use cases
Successor to FRMCS: millimetre wave for railways
    e.g. How to deal with handover / cell change at high speed?

## Slide 13: Future of RMR
EC harmonisation, including FRMCS, expected in H1 2021
A lot of technical studies ongoing within CEPT
RMR cab-radios (GSM-R/FRMCS) may need improved receiver characteristics to filter MFCN emissions above 925 MHz and SRD ones below 919.4 MHz

## Slide 14
ECC Contact: | Web: www.cept.org/ecc
ECO Nyropsgade 37, 4 DK-1366 Copenhagen Tel: +45 33 89 63 00 | 
WG FM Contact:
Thomas Weilacher
thomas.weilacher@bnetza.de
Tel: +49 6131 183119

## Slide 15: Abbreviations
BS | Base Station
EC | European Commission
FM | Frequency Management
FRMCS | Future Railway Mobile Communication System
HO | Handover
INR | Interference to Noise Ratio
LRTC | Least Restrictive Technical Conditions
LTE | Long Term Evolution (4G)
MFCN | Mobile/Fixed Communications Networks
NR | New Radio (5G)
PMSE | Programme Making and Special Events
PT | Project Team
RB | Resource Block
RMR | Railway Mobile Radio
SE | Spectrum Engineering
SRD | Short-Range Devices