# Example - TETRA MS interferers the BS of the analogue FM PMR

## Scenario overview

This section provides an example of sharing studies including an analysis of a TETRA MS interfering with an FM BS, based on the information provided in the ERC Report 104 on “Adjacent Band Compatibility Of 400 MHz TETRA And Analogue FM PMR –  An Analysis Completed Using MONTE CARLO Based Simulation Tool”. This scenario involves a population of TETRA mobile stations interfering with a victim FM base station as shown in Figure 1. In all of the simulations the victim FM system is assumed to have a 7.8 km cell radius which provides a 90 % area availability.

Figure 1: Scenario of the simulation

Figure 2 illustrates the band plan assumed for this investigation. 2 MHz of spectrum has been allocated to the up-link of TETRA and directly adjacent to this, 2 MHz has been allocated to FM.

Figure 2: Band allocations of TETRA MS and FM BS systems

The purpose of this example of simulation is to use SEAMCAT to obtain the probability of interference resulting from unwanted emissions of the TETRA Mobile Stations falling at the frequency where the FM Base Station is operating.

## Characteristics of the systems

### Victim link characteristics – FM

The victim FM system is assumed to have a 7.8 km cell radius which provides a 90% area availability. The reception bandwidth of the FM BS victim receiver is equal to 8 kHz. Based on information provided in ERC Report 104 for FM system based on 12.5 kHz channel spacing, the following characteristics are used to describe the FM equipment:

| Parameter | Mobile Station | Base Station |
| --- | --- | --- |
| Channel Spacing | 12.5 kHz | 12.5 kHz |
| Transmit Power | 37 dBm | 44 dBm |
| Receiver Bandwidth | 8 kHz | 8 kHz |
| Antenna Height | 1.5 m | 30 m |
| Antenna Gain | 0 dBi | 9 dBi |
| Active Interferer Density Range | Variable | Variable |
| Receiver Sensitivity | - 107 dBm | - 110 dBm |
| Receiver Protection Criterion (C/I) | 21 dB | 21 dB |
| Power Control Characteristic | Not used | Not used |

Table 1: Parameters assumed for 12.5 kHz FM  systems

Note 1: This exercise assumes that the noise floor is small compared to the interfering signal (I).

Note 2: The Noise Floor can be obtained using the following equation (see ERC Report 68)

Noise Floor = Sensitivity – Receiver Protection Ratio

| Frequency Offset | Base Station |
| --- | --- |
| Any frequency | - 23 dBm |

Table 2: Receiver blocking for 12.5 kHz FM systems

### Interfering link characteristics – TETRA

The interfering TETRA system is assumed to have a 18 kHz emission bandwidth and a channel spacing which is equal to 25 kHz. The distribution in terms of frequency use over the 2 MHz band is taken as a uniform distribution, where each channel is being assigned the same probability. Based on information provided in ERC Report 104 for TETRA system based on 25 kHz channel spacing, the following characteristics are used to describe the TETRA equipments:

| Parameter | Mobile Station | Base Station |
| --- | --- | --- |
| Channel Spacing | 25 kHz | 25 kHz |
| Transmit Power | 30 dBm | 40 dBm |
| Receiver Bandwidth | 18 kHz | 18 kHz |
| Antenna Height | 1.5 m | 30 m |
| Antenna Gain | 0 dBi | 11 dBi |
| Active Interferer Density Range | Variable | Variable |
| Receiver Sensitivity | - 103 dBm | - 106 dBm |
| Receiver Protection Criterion (C/I) | 19 dB | 19 dB |
| Power Control Characteristic | 5 dB steps to a maximum of 15 dB. Threshold = - 86 dBm | Not used |

Table 3: Parameters used to model the TETRA systems

| Frequency Offset | 30 dBm Mobile Station | Attenuation in dBc |
| --- | --- | --- |
| 25 kHz | - 30 dBm | 60 |
| 50 kHz | - 36 dBm | 66 |
| 75 kHz | - 36 dBm | 66 |
| 100 - 250 kHz | - 45 dBm | 75 |
| 250 - 500 kHz | - 50 dBm | 80 |
| > 500 kHz | - 70 dBm | 100 |

Table 4: Unwanted emissions for TETRA systems (measurement bandwidth of 18 kHz) (interfering transmitter)

## Assumptions

Starting from the characteristics provided above, some “reference” hypothesis might be used to obtain a first set of results.

### Distribution of the Mobile Stations (MS) and propagation model

It is assumed that all mobile stations are located uniformly distributed in the areas around their base stations. For worst case consideration a rural area may be assumed.

### TETRA network

A 2 MHz band is available for TETRA systems of 25 kHz channel spacing, therefore a total of 80 channels are available. It is supposed that only one TETRA MS terminal may use the same frequency at a given time.

The frequency cluster is taken equal to 9, this leads to have 80/9 = 8.88 frequency per cell available. Then up to 9 terminals may be deployed in a TETRA cell.

If the TETRA cell is a traffic limited network and the density of terminals is equal to 5 terminals per km², then the coverage radius is given by the following formula (see ERC Report 68 or User Documentation):

The radius of the cell of the interfering system is given by

R = sqrt( (80*1) / (3.14*5*9) ) = 0.7523 km.

Figure 3 describes a TETRA network based on the above assumptions.

Figure 3: TETRA network based on these assumptions

### Interference situation

As a worst case assumption, we may suppose that, the FM BS station will be based in the TETRA cell where the channel (411.9875 MHz) operating close to the edge of the TETRA band is used. The same probability is assigned to each channel available in the TETRA cell. Then the frequency plan in this cell starts from 410.0125 MHz up to 411.9875  MHz with a step of 25 kHz x 9. A discrete uniform distribution for frequency can be selected, e.g., between 410.0125 MHz and 411.9875 MHz having a step of 25 kHz.

If there is no spatial correlation between the elements of the victim system and the elements of the interfering system then the simulation radius of the simulation is given by the formula:

= radius of the area where interferers are uniformly spread

We have to consider 9 active interferers with a density of 5 terminals/km². Then the radius of simulation area results in:

R = sqrt( 9 / (3.14 x 5) ) = 0.7569 km.

The FM Base Station, which is the victim receiver, is supposed to be operating at 412.00625 MHz, that is the centre of the first channel, i.e. no guard interval is assumed.

### Emission mask

The total emission of the interfering transmitter consists of

- the wanted signal within the defined bandwidth corresponding to a frequency offset of ± 50 % of the emission bandwidth ItBW

- the out-of-band emission caused by the modulation within, e.g. ± 50...250 % of ItBW

- the spurious emission outside these ranges.

This means the mask to be defined has to cover this whole range. This allows co-channel consideration as well.

It should be noted that the TETRA MS unwanted emissions mask is not defined for frequency offsets below 12.5 kHz. Considering the channel spacing of 25 kHz and assuming 0 dBc/18 kHz in that range, then in the undefined range between 12.5 and 25 kHz, a linear interpolation between 0 and 60 dBc attenuation will be performed. It should also be taken into account that the reference bandwidth (18 kHz) used for the mask is identical to the bandwidth of the interfering system.

## Probability of interference

Based on the above assumptions the probability of interference (C/I criteria and unwanted emissions + blocking are taken into account) is about 1.1 % when the PC is “on” and about 8.1 % when the PC is “off”.

## Step-by-step Exercise

In this chapter, only the necessary inputs are mentioned. All other parameters are not required.

| Definition of the workspace, name: "TETRA-PMR" Victim link/General Reference: PMR Frequency:......... MHz (channel spacing) Use wanted transmitter: yes Victim Receiver General Reference: PMR-BS C/I: ... dB (if only C/I, C/(N+I) and (I+N)/N are not required) C/(I+N) ... dB (C/(N+I) required only for selected Blocking-Mode) Noise floor: -131 dBm, constant(=Sensitivity – C/I) Blocking response: -23 dB, constant Blocking mode: Sensitivity Sensitivity: ..... dBm Bandwidth receiver: ...... kHz Antenna height: ... m, constant Antenna azimuth: 0...360 deg, uniform Antenna elevation: 0 deg, constant (horizontal direction) Antenna Reference: PMR-BS Description: Omni-directional Maximum gain: .... dBi Wanted Transmitter General Reference: PMR-MS Power: ...... dBm, constant Antenna height: 1.5 m, constant Antenna azimuth: 0...360 degrees, uniform Antenna elevation: 0 degrees, constant (horizontal direction) | Antenna Reference: PMR-MS Description: Omni-directional Maximum gain: ..... dBi Wt-Vr path Coverage radius Computation of the cell radius: User-defined radius Fixed radius: ..... km Correlation: No (for Wt-Vr) Radio path length: uniform polar (Distance Vr: (0...1)*cell radius) Path Azimuth Vr: 0...360 deg, uniform Propagation model Model: Hata Median Loss: Yes Variation: Yes Environment: RURAL (results in lowest path attenuation) ...at Wt: OUTDOOR ...at Vr: OUTDOOR Propagation: ABOVE ROOF (caused by 30m BS-Antenna height) Interfering link 1/General Reference: TETRA-PMR-ILK1 Frequency: ................................. MHz, uniform Interfering Transmitter General Reference: TETRA-MS Transmitting power: 30 dBm, constant |
| --- | --- |

| Unwanted mask: Offset in MHz, power in dBc referred to Reference bandwidth -10.0000 -100.0000 18.0000 -0.5010 -100.0000 18.0000 -0.5000 -80.0000 18.0000 -0.2510 -80.0000 18.0000 -0.2500 -75.0000 18.0000 -0.1000 -75.0000 18.0000 -0.0750 -66.0000 18.0000 -0.0500 -66.0000 18.0000 -0.0250 -60.0000 18.0000 -0.0125 0.0000 18.0000 0.0125 0.0000 18.0000 0.0250 -60.0000 18.0000 0.0500 -66.0000 18.0000 0.0750 -66.0000 18.0000 0.1000 -75.0000 18.0000 0.2500 -75.0000 18.0000 0.2510 -80.0000 18.0000 0.5000 -80.0000 18.0000 0.5010 -100.0000 18.0000 10.0000 -100.0000 18.0000 Unwanted emission floor: NO Transmitting bandwidth: .... kHz (Bandwidth < channel) Reference bandwidth: .... kHz Power Control: YES PC-Step: ... dB Minimal received power: .... dBm Maximum received power: .... dBm Antenna height: 1.5 m, constant Antenna azimuth: 0...360 degrees, uniform Antenna elevation: 0 degrees, constant (horizontal direction) Power control (at receiver) Power control step: ..... dB Min threshold: ..... dBm Dynamic range: ..... dBm Antenna Reference: TETRA-MS Description: Omni-directional Maximum gain: 0 dBi Wanted Receiver (only for power control) General Reference: TETRA-BS | Antenna height: 30 m, constant Antenna azimuth: 0...360 degrees, uniform Antenna elevation: 0 degrees, constant (horizontal direction) Antenna Reference: TETRA-BS Description: Omni-directional Maximum gain: … dBi It-Vr path Relative location Correlation mode: Uniform density Path Azimuth Vr: 0...360 degrees, uniform Number of active interferers: ..... Density of active interferers: .... users/km² Probability of transmission: 1 (transmits permanently) Activity per hour: 1 (transmits permanently) Protection distance: 0 km Propagation model Model: .................... Median Loss: Yes Variation: Yes Environment: RURAL ...at Wt: OUTDOOR ...at Vr: OUTDOOR Propagation: ABOVE ROOF It-Wr path (only for power control!) Computation of the radio coverage of the interferer Correlation: No (for It-Wr) Mode: Traffic-limited network Density of interferers: .... users/km² Number of channels: .... Number of user per channel: 1 users/ch Frequency cluster: .... Path distance Factor: uniform polar (Distance: (0...1)*cell radius) Path Azimuth: 0...360 degrees, uniform |
| --- | --- |

| Propagation model Model: .................... Median Loss: Yes Variation: Yes Environment: RURAL ...at Wt: OUTDOOR ...at Vr: OUTDOOR Propagation: ABOVE ROOF Simulation control/Event generation Number of samples: 20000 (Default: 20000) Test of the simulation Calculated radius Cell radius of the wanted system: …. km ..interfering system 1: …. km ..simulation radius 1: …. km Generated Signals PC “on” dRSS: mean: …. dBm, std: …. dB iRSSunwanted: mean: …. dBm, std: …. dB iRSSblocking: mean: …. dBm, std: …. dB PC “off” dRSS: mean: …. dBm, std: …. dB iRSSunwanted: mean: …. dBm, std: …. dB iRSSblocking: mean: …. dBm, std: …. dB Interference calculation/ICE calculation Interference Criteria: C/I Compatibility mode: Yes (Probability of interference) Unwanted emissions: Yes Blocking" Yes Result Probability: …. (= …. %) |  |
| --- | --- |

# Footnotes

The level of unwanted emissions is supposed to be constant for frequency offset higher than 500kHz