Answers to the Tetra vs FM PMR example

| Definition of the workspace, name: "TETRA-PMR" Victim link/General Reference: PMR Frequency: 412.00625 MHz (channel spacing) Use wanted transmitter: yes Victim Receiver General Reference: PMR-BS C/I: 21 dB (if only C/I, then C/(N+I) and (I+N)/N are not required) C/(I+N): 21dB (C/(N+I) required only for selected Blocking-Mode) Noise floor: -131 dBm, constant(=Sensitivity – C/I) Blocking response: -23 dB, constant Blocking mode: Sensitivity Sensitivity: -110 dBm Bandwidth receiver: 8 kHz Antenna height: 30 m, constant Antenna azimuth: 0...360 deg, uniform Antenna elevation: 0 deg, constant (horizontal direction) Antenna Reference: PMR-BS Description: Omni-directional Maximum gain: 9 dBi Wanted Transmitter General Reference: PMR-MS Power: 37 dBm, constant Antenna height: 1.5 m, constant Antenna azimuth: 0...360 degrees, uniform Antenna elevation: 0 degrees, constant (horizontal direction) | Antenna Reference: PMR-MS Description: Omni-directional Maximum gain: 0 dBi Wt-Vr path Coverage radius Cell radius mode: User-defined radius Fixed radius: 7.8 km Correlation: No (for Wt-Vr) Radio path length: uniform polar (Distance Vr: (0...1)*cell radius) Path Azimuth Vr: 0...360 deg, uniform Propagation model Model: Hata Median Loss: Yes Variation: Yes Environment: RURAL (results in lowest path attenuation) ...at Wt: OUTDOOR ...at Vr: OUTDOOR Propagation: ABOVE ROOF (caused by 30m BS-Antenna height) Interfering link 1/General Reference: TETRA-PMR-ILK1 Frequency: 410.1875…411.9875 MHz, uniform Interfering Transmitter General Reference: TETRA-MS Transmitting power: 30 dBm, constant |
| --- | --- |

| Unwanted mask: Offset in MHz, power in dBc referred to Reference bandwidth -10.0000 -100.0000 18.0000 -0.5010 -100.0000 18.0000 -0.5000 -80.0000 18.0000 -0.2510 -80.0000 18.0000 -0.2500 -75.0000 18.0000 -0.1000 -75.0000 18.0000 -0.0750 -66.0000 18.0000 -0.0500 -66.0000 18.0000 -0.0250 -60.0000 18.0000 -0.0125 0.0000 18.0000 0.0125 0.0000 18.0000 0.0250 -60.0000 18.0000 0.0500 -66.0000 18.0000 0.0750 -66.0000 18.0000 0.1000 -75.0000 18.0000 0.2500 -75.0000 18.0000 0.2510 -80.0000 18.0000 0.5000 -80.0000 18.0000 0.5010 -100.0000 18.0000 10.0000 -100.0000 18.0000 Unwanted emission floor: NO Transmitting bandwidth: 18 kHz (Bandwidth < channel) Reference bandwidth: 18 kHz Power Control: YES Antenna height: 1.5 m, constant Antenna azimuth: 0...360 degrees, uniform Antenna elevation: 0 degrees, constant (horizontal direction) Power control (at receiver) Power control step: 5 dB Min threshold: -86 dBm Dynamic range: 15 dB Antenna Reference: TETRA-MS Description: Omni-directional Maximum gain: 0 dBi Wanted Receiver (only for power control) General Reference: TETRA-BS Antenna height: 30 m, constant | Antenna azimuth: 0...360 degrees, uniform Antenna elevation: 0 degrees, constant (horizontal direction) Antenna Reference: TETRA-BS Description: Omni-directional Maximum gain: 11 dBi It-Vr path Relative location Correlation mode: Uniform density Path Azimuth Vr: 0...360 degrees, uniform Number of active interferers: 9 Density of active interferers: 5 users/km² Probability of transmission: 1 (transmits permanently) Activity per hour: 1 (transmits permanently) Protection distance: 0 km Propagation model Model: Hata Median Loss: Yes Variation: Yes Environment: RURAL ...at Wt: OUTDOOR ...at Vr: OUTDOOR Propagation: ABOVE ROOF It-Wr path (only for power control!) Computation of the radio coverage of the interferer Correlation: No (for It-Wr) Mode: Traffic-limited network Density of interferers: 5 users/km² Number of channels: 80 Number of user per channel: 1 users/ch Frequency cluster: 9 Path distance Factor: uniform polar (Distance: (0...1)*cell radius) Path Azimuth: 0...360 degrees, uniform |
| --- | --- |

| Propagation model Model: Hata Median Loss: Yes Variation: Yes Environment: RURAL ...at Wt: OUTDOOR ...at Vr: OUTDOOR Propagation: ABOVE ROOF Simulation control/Event generation Number of samples: 20000 Test of the simulation Calculated radius Coverage radius (wanted system): 7.8 km Coverage radius (interfering system 1): 0.752 km simulation radius 1: 0.7569 km Generated Signals PC “on” dRSS: mean: -69.7 dBm, std: 11.8 dB iRSSunwanted: mean: -127.7 dBm, std: 10.0 dB iRSSblocking: mean: -144.6 dBm, std: 7.1 dB PC “off” dRSS: mean: -69.7 dBm, std: 11.8 dB iRSSunwanted: mean: -112.6 dBm, std: 10.8 dB iRSSblocking: mean: -129.6 dBm, std: 7.1 dB Interference calculation/ICE calculation Interference Criteria: C/I Compatibility mode: Yes (Probability of interference) Unwanted emissions: Yes Blocking" Yes Result Probability: 1.1 % when PC “on” and 8.1 % when PC “off” |  |
| --- | --- |